## Slide 1: WF on CCIM UE Behavior during C-DRX
LG Electronics
3GPP TSG-RAN WG4 Meeting #78bis
San Jose del Cabo, Mexico, 11 – 15 April, 2016
Agenda Item: 6.3.1
R4-161934

## Slide 2: Background
RAN4 agreed that
  Baseline receiver for control channel is MRC receiver.
  Reference receivers structure for control channel IM (CCIM) as follows:
    PDCCH/PCFICH/PHICH for synchronous network
      LMMSE-IRC + CRS-IC
      ELMMSE-IRC + CRS-IC
RAN4 will define performance requirement for CCIM receiver in Connected mode.
It is difficult to define performance requirement for CCIM receiver in C-DRX mode.
  Need to clarify CCIM UE behavior during OnDuration.

## Slide 3: In C-DRX Mode
Reference CCIM receivers are requiring higher computational complexity and power consumption comparing with baseline receiver.
By using CCIM receiver during OnDuration, UE power consumption would be increased
  This is against the original purpose of DRX which is UE power saving.
Proposal
  When UE with CCIM capability switches over to C-DRX mode for power saving,
    CCIM receiver is should be allowed to fall back to baseline receiver as its behavior during OnDuration.