## Slide 1
3GPP TSG-RAN WG4 #78BIS
San Jose, Del Cabo, Mexico, 11 – 15 April, 2016
Agenda item: 7.13.1
LG Electronics
WF on adjacent channel coexistence scenarios and parameters at 5.9GHz
R4-162050

## Slide 2: Objective
Define adjacent channel coexistence evaluations scenarios and parameters at 5.9GHz V2V Services during 3 meeting times in RAN WG4. (restricted time limit to complete V2V Core requirements)
5.9GHz operating frequency
  Adjacent channel coexistence evaluation with DSRC/802.11p in ITS spectrum
  Consider following interference scenarios
    V2V UE-to-DSRC UE
    DSRC UE-to-V2V UE
  Deployment simulation parameters based on TR36.885

## Slide 3: Coexistence Scenarios at 5.9GHz
Case 1 (Aggressor-Victim)
  V2V UE-to-DSRC UE
Case 2 (Aggressor-Victim)
  DSRC UE-to-V2V UE
  Consider V2V based on PC5 operation at 5.9GHz
    No LBT mechanism for LTE based V2V UE, follow resource Schedule Assignment (SA).
  DSRC deployment simulation parameters are used
    Max. output power of UE: 23dBm/33dBm
    Unwanted emission limits and adjacent channel rejection
DSRC
V2V
f
V2V
DSRC
f

## Slide 4: General paramters
Deployment scenarios: Urban case
Simulation Block Size :
  Urban : Manhattan grid model: 3*433m, 3* 250m (in page 6)
Absolute vehicle speed for urban
  Urban : 15km/h, 60km/h
  Used only to decide vehicle density.
  Fixed location will be considered for adjacent coexistence evaluation.
  Vehicle density : Follow TR36.885
  # of activate UEs per V2V cell: Round (5% * # of total dropped UEs/cell)
  # of activate UEs per DSRC cell: 1UE (whole BW)

## Slide 5: Parameters at 5.9GHz operating frequency
Only consider outdoor deployment
Pathloss models
  V2V UE-to-DSRC UE : Follow TR 36.885
  DSRC UE-to-V2V UE : Follow TR36.885
ACLR and ACS values for DSRC UE (10MHz)
  UE ACLR=26dB (max. Power 23dBm)/ 38dB(max. Power 33dBm)
  UE ACS=34/37/40dB
ACLR and ACS values for V2V UE (10MHz)
  UE ACLR=30dB, UE ACS=33dB
  For power class 3 V2V UE, RAN4 consider ACLR1 and ACLR2
Detail parameters can be revised in future meeting.

## Slide 6: Evaluation methodology
Static simulations
  Monte-carlo based static simulations.
Evaluation metric
  DSRC system Throughput degradation due to adjacent channel interferer(s)
  Need further discussion on evaluation metric for the V2V victim scenarios.
    Encourage vendors to provide their view on this since RAN1 has ongoing discussion on the detail of the parameters (e.g. RB allocation and RS design)

## Slide 7: Way Forward
Coexistence scenarios
  Coexistence Scenario (Aggressor-Victim) at 5.9GHz operating frequency
    V2V UE-to-DSRC UE
    DSRC UE-to-V2V UE
Coexistence parameters
  Consider these proposed parameters to evaluate adjacent channel coexistence at 5.9GHz