## Slide 1: WF on DL Control Channel IM UE Capabilities
Intel Corporation, ZTE
3GPP TSG-RAN WG4 Meeting #78bis San Jose del Cabo, Mexico, 11 – 15 Apr 2016
Agenda Item: 6.3
R4-162757

## Slide 2: Background
RAN #78 agreements:
  Two types of reference IM Receiver structures for PDCCH/PCFICH/PHICH in synchronous networks
    Type A IM receiver: LMMSE-IRC + CRS-IC
    Type B IM receiver: E-LMMSE-IRC + CRS-IC
  Define different UE capabilities for the two types of IM Receiver structures
    UE Capability #1: Support Type A IM receiver
    UE Capability #2: Support Type B IM receiver
RAN4 78bis agreements
  UE capabilities signalling is needed
  Single UE capability should be defined for all DL control channels

## Slide 3: Way Forward (1)
DL Control Channel IM receivers applicability
Type A CCIM capability is the pre-requisite capability for Type B CCIM receiver capability. UEs with Type B CCIM receiver should support Type A CCIM processing.
UE capabilities signalling will be introduced for DL Control Channel IM feature
  Option1:
    Bit #1: Support of Type A DL Control IM receiver capability
    Bit #2: Support of Type B DL Control IM receiver capability for PDCCH/PCFICH/PHICH receive processing in synchronous networks
  Option2:
    Bit #1: Support of generic Dl Control Channel IM capabilities. Depending on whether UE supports Type A/B processing it will pass different test cases to confirm the capability.
 | PDCCH/PCFICH/PHICH |  | EPDCCH | 
 | Synchronous networks | Asynchronous networks | Synchronous networks | Asynchronous networks
Type A receiver | LMMSE-IRC + CRS-IC | FFS | LMMSE-IRC + CRS-IC | LMMSE-IRC
Type B receiver | E-LMMSE-IRC + CRS-IC | NA | NA | NA

## Slide 4: Way Forward (2)
Capability signalling method
  Option 1
    Per UE capability signalling. Signalling provided under assumption that UE supports feature on at least one CC. UE does not provide the information of supported CCs.
  Option 2
    Per CC capability signalling. Details FFS.
Decision on UE capabilities to be made in RAN4 #79