## Slide 1: Way forward on 4Rx RI reporting
Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-162772
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background
Agreement
  Agree same condition existing test 1 to 3 with further discussion on the detailed test metric
  Low correlation for 3-4 layer if we have option 1

## Slide 3: Assumptions CRS (FDD) from 9.5.1.1
Parameter |  | Unit | Test 1 | Test 2 | Test 3 | Test 4
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 4 |  |  | 
Downlink power allocation |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | 0 |  |  | 
Propagation condition and antenna configuration |  |  | 2 x 4 EPA5 |  |  | 4 x 4 EPA5
CodeBookSubsetRestriction bitmap |  |  | 000011 for fixed RI = 1 010000 for fixed RI = 2 010011 for UE reported RI |  |  | TBD
Antenna correlation |  |  | Low | Low | High | Low
RI configuration |  |  | Fixed RI=2 and follow RI | Fixed RI=1 and follow RI | Fixed RI=1 and follow RI | Fixed RI=2 and follow RI
SNR |  | dB | 0 | 20 | 20 | TBD
 |  | dB[mW/15kHz] | -98 | -98 | -98 | -98
 |  | dB[mW/15kHz] | -98 | -78 | -78 | TBD
Maximum number of HARQ transmissions |  |  | 1 |  |  | 
Reporting mode |  |  | PUCCH 1-1 (Note 4) |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUCCH Format 2 |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUSCH (Note 3) |  |  | 
PUCCH Report Type for RI |  |  | 3 |  |  | 
Reporting periodicity |  | ms | Npd= 5 |  |  | 
PMI and CQI delay |  | ms | 8 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 6 |  |  | 
ri-ConfigurationInd |  |  | 1 (Note 5) |  |  | 

## Slide 4: Assumption RI test CRS (FDD)
 | Test 1 | Test 2 | Test 3 | Test 4
g1 | N/A | 1.05 | 0.9 | N/A
g2 | 1 | N/A | N/A | TBD
UE Category | ≥2 | ≥2 | ≥2 | 

## Slide 5: Assumptions CRS (TDD) from 9.5.1.2
Parameter |  | Unit | Test 1 | Test 2 | Test 3 | Test 4
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 4 |  |  | 
Downlink power allocation |  | dB | -3 |  |  | 
 |  | dB | -3 |  |  | 
 |  | dB | 0 |  |  | 
Uplink downlink configuration |  |  | 2 |  |  | 
Special subframe configuration |  |  | 4 |  |  | 
Propagation condition and antenna configuration |  |  | 2 x 4 EPA5 |  |  | 4 x 4 EPA5
CodeBookSubsetRestriction bitmap |  |  | 000011 for fixed RI = 1 010000 for fixed RI = 2 010011 for UE reported RI |  |  | TBD
Antenna correlation |  |  | Low | Low | High | Low
RI configuration |  |  | Fixed RI=2 and follow RI | Fixed RI=1 and follow RI | Fixed RI=1 and follow RI | Fixed RI=2 and follow RI
SNR |  | dB | 0 | 20 | 20 | TBD
 |  | dB[mW/15kHz] | -98 | -98 | -98 | -98
 |  | dB[mW/15kHz] | -98 | -78 | -78 | TBD
Maximum number of HARQ transmissions |  |  | 1 |  |  | 
Reporting mode |  |  | PUSCH 3-1 (Note 3) |  |  | 
Reporting interval |  | ms | 5 |  |  | 
PMI and CQI delay |  | ms | 10 or 11 |  |  | 
ACK/NACK feedback mode |  |  | Bundling |  |  | 

## Slide 6: Assumption RI test CRS (TDD)
 | Test 1 | Test 2 | Test 3 | Test 4
g1 | N/A | 1.05 | 0.9 | N/A
g2 | 1 | N/A | N/A | TBD
UE Category | ≥2 | ≥2 | ≥2 | 

## Slide 7: Assumptions CSI-RS (FDD) from 9.5.2.1
Parameter |  | Unit | Test 1 | Test 2 | Test 3 | Rank 3
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 | Pc | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
Propagation condition and antenna configuration |  |  | 2 x 4 EPA5 |  |  | 4 x 4 EPA5
Cell-specific reference signals |  |  | Antenna ports 0 |  |  | 
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CSI reference signals |  |  | Antenna ports 15, 16 |  |  | Antenna ports 15-18
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/1 |  |  | 
CSI reference signal configuration |  |  | 6 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 000011 for fixed RI = 1 010000 for fixed RI = 2 010011 for UE reported RI |  |  | TBD
Antenna correlation |  |  | Low | Low | High | Low
RI configuration |  |  | Fixed RI=2 and follow RI | Fixed RI=1 and follow RI | Fixed RI=1 and follow RI | Fixed RI=2 and follow RI
SNR |  | dB | 0 | 20 | 20 | TBD
 |  | dB[mW/15kHz] | -98 | -98 | -98 | -98
 |  | dB[mW/15kHz] | -98 | -78 | -78 | -78
Maximum number of HARQ transmissions |  |  | 1 |  |  | 
Reporting mode |  |  | PUCCH 1-1 |  |  | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note 3) |  |  | 
PUCCH Report Type for CQI/PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUCCH Format 2 |  |  | 
PUCCH Report Type for RI |  |  | 3 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
PMI and CQI delay |  | ms | 8 |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 2 |  |  | 
ri-ConfigurationInd |  |  | 1 (Note 4) |  |  | 

## Slide 8: Assumption RI test CSI-RS (FDD)
 | Test 1 | Test 2 | Test 3 | Rank 3 test
g1 | N/A | 1.05 | 0.9 | N/A
g2 | 1 | N/A | N/A | N/A
g3 |  |  |  | TBD
UE Category | ≥2 | ≥2 | ≥2 | 

## Slide 9: Assumptions CSI-RS (TDD) from 9.5.2.2
Parameter |  | Unit | Test 1 | Test 2 | Test 3 | Test 4
Bandwidth |  | MHz | 10 |  |  | 
PDSCH transmission mode |  |  | 9 |  |  | 
Downlink power allocation |  | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
 | Pc | dB | 0 |  |  | 
 |  | dB | 0 |  |  | 
Uplink downlink configuration |  |  | 1 |  |  | 
Special subframe configuration |  |  | 4 |  |  | 
Propagation condition and antenna configuration |  |  | 2 x 4 EPA5 |  |  | 4 x 4 EPA5
Cell-specific reference signals |  |  | Antenna ports 0 |  |  | 
CSI reference signals |  |  | Antenna ports 15, 16 |  |  | Antenna ports 15-18
Beamforming Model |  |  | As specified in Section B.4.3 |  |  | 
CSI reference signal configuration |  |  | 4 |  |  | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/4 |  |  | 
CodeBookSubsetRestriction bitmap |  |  | 000011 for fixed RI = 1 010000 for fixed RI = 2 010011 for UE reported RI |  |  | TBD
Antenna correlation |  |  | Low | Low | High | Low
RI configuration |  |  | Fixed RI=2 and follow RI | Fixed RI=1 and follow RI | Fixed RI=1 and follow RI | Fixed RI=2 and follow RI
SNR |  | dB | 0 | 20 | 20 | TBD
 |  | dB[mW/15kHz] | -98 | -98 | -98 | -98
 |  | dB[mW/15kHz] | -98 | -78 | -78 | TBD
Maximum number of HARQ transmissions |  |  | 1 |  |  | 
Reporting mode |  |  | PUCCH 1-1 |  |  | 
Physical channel for CQI/ PMI reporting |  |  | PUSCH (Note 3) |  |  | 
PUCCH report type for CQI/ PMI |  |  | 2 |  |  | 
Physical channel for RI reporting |  |  | PUCCH Format 2 |  |  | 
Reporting periodicity |  | ms | Npd = 5 |  |  | 
PMI and CQI delay |  | ms | 10 |  |  | 
ACK/NACK feedback mode |  |  | Bundling |  |  | 
cqi-pmi-ConfigurationIndex |  |  | 4 |  |  | 
ri-ConfigurationInd |  |  | 1 |  |  | 

## Slide 10: Assumption RI test CSI-RS (TDD)
 | Test 1 | Test 2 | Test 3 | Rank 3 test
g1 | N/A | 1.05 | 0.9 | N/A
g2 | 1 | N/A | N/A | TBD
UE Category | ≥2 | ≥2 | ≥2 | 

## Slide 11: Way Forward
Evaluate for each section the requirements for Test 1 to 3 with 4Rx
Evaluate Test 4 (Rank 3-4) for each section. The purpose is to check that the UE for high SNR signals rank 3 and/or rank 4 and thereby get higher throughput than fixed rank 2
TBDs to be discussed over email
Evaluation results to be presented with throughput for fixed and follow RI as well as the gamma values for the evaluated SNRs
Propose Alignment and Impairment