## Slide 1: WF on REFSENS for NB-IoT
Sony, ……
R4-162828
3GPP TSG RAN WG1 #84 bis
San Jose del Cabo, Mexico, 11 - 15 April, 2016
Agenda item 6.23.3

## Slide 2: Background
Legacy REFSENS calculation
PREFSENS (dBm)= -174dBm + 10log10B+NF + IM + Rb + SNR
    -174dBm noise floor at room temperature in 1Hz (1.38*10-23*300)
    B operating bandwidth in Hz
    NF Noise figure in dB of the receiver in antenna connector
    IM Implementation and production margin
    Rb Band dependant relaxation factor
    SNR Required Signal to Noise Ratio in baseband

## Slide 3: Background
Option 1 Re-use the existing (legacy) REFSENS table and apply the same relaxation for single RX as was agreed for cat 0. Then there would be a scaling from the 5MHz value of 10log10(1RB/25RB) = -14dB. The assumption in this case is that the same SNR for NB IOT as for legacy LTE applies. There is also a band-dependant factor in legacy LTE whose relevance needs to be discussed since only half duplex is considered.
Option 2 The alternative method would be to start all over: determine required SNR (e.g. by simulation), estimate the noise figure for the receiver, and agree on an adequate implementation and production margin. The noise figure of the receiver need to be calculated in antenna connector and may have some frequency dependence (e.g. above/below 1GHz or something). Probably there has to be an agreement on possible reference architectures (SAW filter, SAW-less or maybe both) in order to do the NF calculation.

## Slide 4: Agreement
Option 2 shall be used in deriving REFSENS for NB IOT

## Slide 5: Actions for 3GPPRAN4#78-NB-IoT
Agree on the following parameters:
  Nf for the NB IOT receiver [8dB] including
    1/f noise
    extreme temperature
  IM for the NB IOT receiver [3dB]
  Band dependent relaxation factor for difficult bands Rb [0 – 1.5dB]
  Bands where apply Rb shall be applied is FFS
Agree on additional requirement/test, e.g. called “Enhanced coverage sensitivity”
Agree on SNR from simulations according to simulation parameters on next page.
Companies are encourage to contribute on the above including SNR simulations.

## Slide 6: Simulation assumptions for SNR
Parameter | Unit | Standalone Case
Channel bandwidth | kHz | 200
Antenna configuration |  | SISO
Allocated resource blocks |  | 1
Subcarriers per resource block |  | 12
Allocated subframes per Radio Frame |  | 10
Channel Coding |  | TBCC
Modulation |  | QPSK
Target Coding Rate |  | 1/3
Maximum number of HARQ transmissions |  | 1
Information Bit Payload per Sub-Frame |  | [88]
Transport block CRC | Bits | 24
Number of Code Blocks per Sub-Frame |  | 1
Binary Channel Bits Per Sub-Frame |  | [320]
LTE CRS ports |  | N/A
NRS ports (even if 2 Tx antennas are not used but REs corresponding to NRS port 1 is still reserved) |  | [0]
Channel estimation |  | [Practical]
Channel |  | AWGN
Frequency error |  | None
Timing error |  | None
Power boosting |  | N/A

## Slide 7: References
R4-162610 NB-IoT UE Rx RF Requirements, MediaTek Inc.
R4-162250 UE REFSENS for NB-IoT, Ericsson
R4-162552 WF on REFSENS for NB IOT, Sony