## Slide 1: WF on LAA Bandwidth combination sets in CA basket work items
Nokia, […..]
R4-162931

## Slide 2: Reference
R4-162164 Inclusion of 10MHz CBW for LAA operation, Ericsson
R4-162279 Bandwidth combination sets for LAA, Nokia
R4-162298 Discussion on channel bandwidth for LAA, Huawei
R4-162294 Considerations on adding 10MHz channel bandwidth for CA combinations with Band 46, Huawei
R4-162647 Addition of 10 MHz channel bandwidth for LAA, Qualcomm
R4-162280 WF on LAA Bandwidth combination sets in CA basket work items, Nokia
R4-162605 LAA 10MHz, Vodafone

## Slide 3: Background
Band 46 was created with 20Mhz in Release 13, while agreement was made that 10, and 15MHz were not precluded in Band 46
Main reason is that in certain locations allowed frequency ranges for unlicensed operation are not multiple of 20MHz and therefore lower BWs than 20MHz are useful for greater spectrum efficiency
Introduction of Band 46 with 10MHz is part of Release 14 WID for eLAA
During RAN#71 all CA basket WIDs were updated using 10MHz for Band 46 while RAN4 was tasked to discuss how to introduce it

## Slide 4: Way forward (1/3)
Applicable release:
10MHz is included in Rel-14 specifications
CA combinations are release independent from Rel-13.
Combination sets:
  For combinations different from those including Bands 1,3,5 and 7, 10MHz was not requested and therefore they do not need to use 10MHz
  For 1+46A 3+46A and 7+46A, 10MHz is included in BCS1 (BSC0 is already in use from Release 13)
  For 5+46A, 10MHz is included in BCS1 in brackets, and BCS0 is for 20MHz only
  Introduce 10MHz to CA_46C, CA_46D and CA_46E as BCS1
    BCS0 is reserved for fallback operations without 10MHz
  For 7A+46C and 7A+46D they refer to BCS1 for 46C,46D,46E respectively (20 and 10MHz), and they are all BCS0
  For 1,5A+46C and 1,5A+46D and 1,5A+46E, two sets are created
    BCS0: they refer to BCS0 for 46C,46D,46E respectively (20 MHz) with all values in brackets
    BCS1: they refer to BCS1 for 46C,46D,46E respectively (20 and 10MHz) with all values in brackets
  There is no consensus on 3+46C, 3+46D, and 3+46E.
  Note that the two combinations sets for 5A+46A, 1,5A+46C and 1,5A+46D and 1,5A+46E will be changed to only one combination set (with 20 and 10MHz) if the associated requirements to include 10MHz are completed by RAN4#79. otherwise two combinations sets remain and brackets removed

## Slide 5: Way forward (2/3)
Raster:
For India, there are two unlicensed allocations that are not multiple of 20MHz
  5725-5875 for Indoor and 5825-5875 for outdoor
For indoor there is a 10MHz channel unused at center frequency 5730MHz
For outdoor there is 10MHz channel unused at center frequency 5830MHz
OUT
INDOOR

## Slide 6: Way forward (3/3)
Raster (cont’d):
CR to 36.104 (red text)
NOTE 3: The following NDL and NUL are allowed for operation in Band 46 assuming 20MHz channel bandwidth: NDL =NUL = {n-2, n-1, n, n+1, n+2 | n = 46890 (5160 MHz), 47090 (5180 MHz), 47290 (5200 MHz), 47490 (5220 MHz), 47690 (5240 MHz), 47890 (5260 MHz), 48090 (5280 MHz), 48290 (5300 MHz), 48490 (5320 MHz), 48690 (5340 MHz), 50090 (5480 MHz), 50290 (5500 MHz), 50490 (5520 MHz), 50690 (5540 MHz), 50890 (5560 MHz), 51090 (5580 MHz), 51290 (5600 MHz), 51490 (5620 MHz), 51690 (5640 MHz), 51890 (5660 MHz), 52090 (5680 MHz), 52290 (5700 MHz), 52490 (5720 MHz), 52740 (5745 MHz), 52940 (5765 MHz), 53140 (5785 MHz), 53340 (5805 MHz), 53540 (5825 MHz), 53740 (5845 MHz), 53940 (5865 MHz), 54140 (5885 MHz), 54340 (5905 MHz)}. And the following NDL and NUL are allowed for operation in Band 46 assuming 10MHz channel bandwidth NDL =NUL = {n-2, n-1, n, n+1, n+2 | n = 52590 (5730 MHz), 53590 (5830 MHz)} . 10 MHz bandwidth shall not be used when overlapping with a 20MHz channel where the absence of non 3GPP technologies cannot be guaranteed on a long term basis (e.g., by level of regulation) unless additional work on channel access is agreed and completed to ensure fair coexistence with these other non 3GPP technologies

## Slide 7: For information
Expected spec changes for 10MHz support in DL
36.104:
  5.7.1 Channel spacing
  5.7.1A CA Channel spacing
  5.7.3 Carrier frequency and EARFCN (handled by this WF)
  6.6.2 Adjacent Channel Leakage power Ratio (ACLR)
  6.6.3 Operating band unwanted emissions
  9.1.1 Channel access parameters
36.101
  7.3 Reference sensitivity power level
  7.5 Adjacent Channel Selectivity (ACS)
  7.6.1 In-band blocking
  7.8 Intermodulation characteristics
Other spec changes may be further identified