## Slide 1: Way forward on performance metric for V2V system
Agenda item: 7.13.1
Source: CATT,Huawei
3GPP TSG-RAN WG4 #78bis R4-163003
San Jose del Cabo, Mexico, 11 – 15 April, 2016

## Slide 2: Background
In RAN4#78 meeting, it was agreed that evaluation metric for the V2V victim scenarios needs further discussion.

## Slide 3: Performance metric
Adopt the Packet Reception Ratio (PRR) defined in RAN1 TR36.885, which is copied as below, as performance metric for V2V system in RAN4 co-existence simulation study.
Packet Reception Ratio (PRR) :
  For one Tx packet, the PRR is calculated by X/Y, where Y is the number of UE/vehicles that located in the range (a, b) from the TX, and X is the number of UE/vehicles with successful reception among Y. CDF of PRR and the following average PRR are used in evaluation
    CDF of PRR with a = 0, b = baseline of 320 meters for freeway and 150 meters for urban. Optionally, b = 50 meters for urban with 15 km/h vehicle speed.
    Average PRR, calculated as (X1+X2+X3….+Xn)/(Y1+Y2+Y3…+Yn) where n denotes the number of generated messages in simulation. with a = i*20 meters, b = (i+1)*20 meters for i=0, 1, …, 25
PRR is determined with the SNR VS. BLER mapping table and/or curve. RAN4 should use the same baseline mapping model in order to align system simulation results. In the system simulation, the acceptable PRR degradation for V2V victim system is FFS.
It is proposed that companies provide link level simulation results for the mapping model based on assumptions in next slide.

## Slide 4: Tentative link level simulation assumption
Parameter | Assumption
Bandwidth | 10Mz
Carrier frequency | 2GHz 5.9GHz
Number of antenna | 1 TX and 2 RX
Fading | The same as ITU-R UMi clustered delay line models (CDL) used in TR36.843
channel | LOS &NLOS
Modulation | QPSK
Coding | Turbo,1/2
TBsize | 190byte
Relative speed | 30km/h 120km/h
Retransmission | Off
The maximum transmission number | 1
synchronization | Ideal (no Synchronization error impact in the simulation)