## Slide 1: Way forward on simulation assumptions for SFN scenario with unidirectional deployment
Ericsson
3GPP TSG-RAN WG4 Meeting #78bis R4-163034
San Jose del Cabo, Mexico, 11-15 April, 2016

## Slide 2: Background
There are no the simulation assumptions agreed for WI phase to facilitate the further evaluation.
Simulation assumptions are needed to further evaluation.

## Slide 3: Background
In #78 meeting, the agreements on scenario assumption is:
  Scenarios assumptions
    Simulation assumptions agreed in SI are treated as baseline, and others assumptions are not precluded.
      Following parameters are encouraged for evaluation.
Parameter | Value | 
 | SFN scenario 1 | SFN scenario 2d
RRH Railway track distance (Dmin) | 300m | 5m
Distance between RRH (Ds) | 1km; 1.5km | 500m
Cell ISD | 2km (2RRHs connect to 1 BBU); 3km (2RRHs connect to 1 BBU) Other number of RRH is not precluded | 1km (2RRHs connect to 1 BBU);
RRH height (compared to railway track) | 25m | 2.5m

## Slide 4: Simulation assumption for Link adaptation
Parameters |  | Unit | Values
Bandwidth |  | MHz | 10
Duplex mode |  |  | FDD
MCS |  |  | Link adaptation with OLLA PUCCH 1-0 periodic CQI feedback mode
Propagation condition and correlation matrix | SFN |  | Dynamic SFN channel model: • Channel model for SFN Scenario1 and 2d, which is specified in 6.4.3.3.1 of TR36.878 as baseline for evaluation. Parameters: • Doppler shift, relative time delay and relative power change with time, which is specified Table 6.4.3.3 of TR36.878 for SFN Scenario 1 and 2d respectively; • Static channel matrix as defined in B.1 in 36.101; • Velocity of train: 500km/h
Antenna configuration |  |  | 2x2
Transmission mode |  |  | TM3
Reference receiver |  |  | • Option 1: Baseline MMSE receiver
Noise estimation |  |  | Practical
Time and frequency track |  |  | Practical

## Slide 5: Simulation assumption for Fixed MCS
Parameters |  | Unit | Values
Bandwidth |  | MHz | 10
Duplex mode |  |  | FDD
MCS |  |  | Option1: MCS#19 (R.35-4 FDD) Option 2: MCS#16 Option 3: MCS#?
Propagation condition and correlation matrix | SFN |  | Dynamic SFN channel model: • Channel model for SFN Scenario1 and 2d, which is specified in 6.4.3.3.1 of TR36.878 as baseline for evaluation. Parameters: • Doppler shift, relative time delay and relative power change with time, which is specified in Table 6.4.3.3 of TR36.878 for SFN Scenario 1 and 2d respectively; • Static channel matrix as defined in B.1 in 36.101; • Velocity of train: 500km/h
Antenna configuration |  |  | 2x2
Transmission mode |  |  | TM3
Reference receiver |  |  | • Option 1: Baseline MMSE receiver
Noise estimation |  |  | Practical
Time and frequency track |  |  | Practical