## Slide 1: Motivation for NB-IoT RF requirement on coexistence with CDMA
China Telecom
3GPP TSG RAN Meeting #72
Nanjing, China, 23 – 27 May, 2016
Agenda item 11
R4-163575

## Slide 2: Justification
R13 NB-IoT RF requirement was specified based on the NB-IoT coexistence with legacy GSM/UMTS/LTE systems.
Currently CDMA coexistence with NB-IoT is not be considered in NB-IoT RF requirement evaluation. It will bring difficulty for CDMA operators to deploy NB-IoT , and also for inter-operator coexistence.

## Slide 3: Justification
CDMA system is widely to be used in many countries such as China, Japan, Korea, US etc. in different regions, the frequency below 2GHz is mainly to be used, while 800M is the most important frequency band for CDMA network to realise wide coverage performance.
CDMA2000 Deployments (includes CDMA2000 1X & EV-DO) |  |  |  |  |  | 
 | Asia - Pacific | North America | Caribbean - Latin America | Europe - Russia | Africa - Middle East | Worldwide
Operators | 73 | 63 | 48 | 59 | 71 | 314
Countries/Territories | 32 | 2 | 24 | 14 | 46 | 118
CDMA2000 Devices by Operating Frequency |  |  |  |  |  |  |  |  | 
 | 450 MHz | 800 MHz | 800/1900 MHz | 1700 MHz | 1900 MHz | 2100 MHz | 800/2100 MHz | 800/1900/ 2100 MHz (AWS) | 800/1900/700/ 1700/2100 MHz (AWS)
1X | 124 | 1065 | 478 | 167 | 96 | 1 | 1 | 7 | 14
1xEV-DO Rel. 0 | 21 | 261 | 210 | 92 | 2 | 0 | 12 | 0 | 8
1xEV-DO Rev. A | 45 | 201 | 394 | 8 | 17 | 7 | 39 | 2 | 25
EV-DO Rev. B | 7 | 2 | 4 | 1 | 0 | 1 | 18 | 0 | 2
1X Advanced | 0 | 0 | 5 | 0 | 0 | 0 | 0 | 0 | 3
Totals | 197 | 1,529 | 1,091 | 268 | 115 | 9 | 70 | 9 | 52

## Slide 4: Justification
In RAN4#78bis meeting, a WF on handling of CDMA and NB-IoT coexistence study was approved in R4-162833, and agreements were reached as below,
  CDMA and NB-IoT coexistence should be studied.
  Considering the tight schedule of R13 NB-IoT, it is recommended such coexistence study be conducted and evaluated in potential R14 WI/SI.

## Slide 5: Objective
  Identify frequency bands for interference evaluation on NB-IoT coexistence with CDMA, such as bands around 800M( B5/B26 etc.)
  For the NB-IoT stand-alone operation mode, evaluate RF requirement for NB-IoT coexistence with CDMA, and if R13 NB-IoT RF requirements could be reused.
  Specify necessary additional RF requirements of NB-IoT to coexist with CDMA.

## Slide 6: Reference
[1]. R4-162833, Way forward on handling of CDMA and NB-IoT coexistence study, China Telecom, SK Telecom, Sprint, Qualcomm, HuaWei, Intel, ZTE, Samsung, 3GPP TSG-RAN WG4 Meeting #78bis,San Jose Del Cabo, 11 – 15 Apr, 2016