## Slide 1: WF: MSD definition for 2UL Inter-band CA combinations that have multiple IMD’s for one band
Huawei, Hisilicon, NTT DOCOMO Inc,
R4-163639
3GPP TSG-RAN WG4 Meeting #79
Nanjing, China, 23-27 May 2016

## Slide 2: Background
Agreement on how 2UL Inter-band CA MSD requirements due to intermodulation exists [1]
  In short, only the worst case MSD is defined for each band
    This means that even if there are multiple IMD’s only the one resulting highest MSD is specified
  This agreement was a result of extensive discussions in RAN4
  All 2UL Inter-band CA combinations (2UL/2DL, 2UL/xDL in 36.101 have been handled according to this agreement
    Out of currently specified 16 combinations, 8 have more than one IMD. In 7 case out of these 8, IMD5 is the second IMD

## Slide 3: Background
Recently B3+B42 UL CA MSD was studied. According to agreed TP, MSD’s are as follows. 29.8dB for IMD2, 8.0dB for IMD4, and 0.2dB for IMD5
An issue was raised to define IMD4 as well
It’s quite likely that there will be cases also in future where there are more than one IMD’s with significant MSD’s
As such, there is nothing wrong or broken in current agreement. However, with this good example of B3+B42 there is good time to slightly further modify it

## Slide 4: Way forward
Proposal1: For each UL Inter-band CA only the highest MSD is specified automatically. Each IMD that falls on top of own DL channel and has ≥3dB MSD will be specified as well. This applies from Rel14 onwards.
Proposal2: A column shall be added in Rel14 UL Inter-band CA MSD tables to tell the source of IMD.
Proposal3: An informative note to UL Inter-band CA MSD tables shall be added in Rel14 to indicate if there are other IMD’s than the specified one(s) for each band.
Proposal 4: Case when two or more IMD’s fall on top of each other is FFS

## Slide 5: Example
E-UTRA Band / Channel bandwidth / NRB / Duplex mode |  |  |  |  |  |  |  | Source of IMD
EUTRA CA Configuration | EUTRA band | UL Fc (MHz) | UL/DL BW (MHz) | UL CLRB | DL Fc (MHz) | MSD (dB) | Duplex mode | 
CA_3A-5A | 3 | 1771 | 10 | 50 | 1866 | 4 | FDD | IMD4
 | 5 | 838 | 5 | 25 | 883 | N/A |  | 
CA_3A-5A | 3 | 1721 | 10 | 50 | 1816 | N/A | FDD | 
 | 5 | 838 | 5 | 25 | 883 | 24 |  | IMD23
CA_3A-7A | 3 | 1730 | 5 | 25 | 1825 | N/A | FDD | 
 | 7 | 2535 | 10 | 50 | 2655 | 13 |  | IMD4
CA_3A-8A | 3 | 1755 | 10 | 50 | 1850 | N/A | FDD | 
 | 8 | 900 | 5 | 25 | 945 | 8 |  | IMD43
CA_3A-19A | 3 | 1771 | 5 | 25 | 1866 | 4 | FDD | IMD4
 | 19 | 838 | 5 | 25 | 883 | N/A |  | 
CA_3A-19A | 3 | 1721 | 5 | 25 | 1816 | N/A | FDD | 
 | 19 | 838 | 5 | 25 | 883 | 27 |  | IMD23
CA_3A-26A | 3 | 1771 | 5 | 25 | 1866 | 4 | FDD | IMD4
 | 26 | 838 | 5 | 25 | 883 | N/A |  | 
CA_3A-26A | 3 | 1721 | 5 | 25 | 1816 | N/A | FDD | 
 | 26 | 838 | 5 | 25 | 883 | 26 |  | IMD23
CA_4A-5A | 4 | 1721 | 5 | 25 | 2121 | N/A | FDD | 
 | 5 | 838 | 5 | 25 | 883 | 26 |  | IMD23
CA_4A-7A | 4 | 1730 | 5 | 25 | 1825 | N/A | FDD | 
 | 7 | 2535 | 5 | 25 | 2655 | 15 |  | IMD4
CA_5A-7A | 5 | 834 | 5 | 25 | 879 | 12 | FDD | IMD33
 | 7 | 2547 | 10 | 50 | 2667 | N/A |  | 
CA_7A-20A | 7 | 2512 | 10 | 50 | 2632 | N/A | FDD | 
 | 20 | 851 | 5 | 25 | 810 | 12 |  | IMD33
CA_3A-42A | 3 | 1740 | 5 | 25 | 1835 | 29.8 | FDD | IMD23
 | 42 | 3575 | 5 | 25 | 3575 | N/A | TDD | 
CA_3A-42A | 3 | 1765 | 5 | 25 | 1835 | 8 | FDD | IMD43
 | 42 | 3435 | 5 | 25 | 3575 | N/A | TDD | 
NOTE 1: Both of the transmitters shall be set min(+20 dBm, PCMAX_L,c) as defined in subclause 6.2.5A NOTE 2: RBSTART = 0 NOTE3: This band is subject to IMD5 as well which MSD is not specified |  |  |  |  |  |  |  | 

## Slide 6: Reference
[1] R4-144031, “WF on 2UL inter-band CA MSD test configurations”, Mediatek, RAN4#71
[2] R4-163636, “MSD definition for 2UL Inter-band CA combinations that have multiple IMD’s for one band”, Huawei, Hisilion, RAN4#79