## Slide 1: Way forward on MSD for Band 8 and Band 41 2UL CA
CMCC, Huawei, HiSilicon, MediaTek
3GPP TSG-RAN WG4 Meeting #79 R4-164696 Nanjing, China, 23 – 27 May, 2016

## Slide 2: Background(1/2)
CA_B8+B41 2UL CA has two intermodulation products IMD3 and IMD5 falling on B8. IMD3 will not fall into the operating band according to operators’ spectrum holding. Therefore, it is not necessary to analyze IMD3 for this CA
UE UL carriers | fx_low | fx_high | fy_low | fy_high
UL frequency (MHz) | 880 | 915 | 2496 | 2690
2nd harmonics frequency limits | 2*fx_low | 2*fx_high | 2* fy_low | 2* fy_high
2nd harmonics frequency limits (MHz) | 1760 – 1830 |  | 4992 – 5380 | 
Two-tone 3rd order IMD products | ¦2*fx_low – fy_high¦ | ¦2*fx_high – fy_low¦ | ¦2*fy_low – fx_high¦ | ¦2*fy_high – fx_low¦
IMD frequency limits (MHz) | 666–930 |  | 4077–4500 | 
IMD5 | IMD 5(MHz)
¦2*fx - 3*fy¦ | 5658 – 6310
¦2*fx + 3*fy¦ | 9318 – 9830
¦2*fy - 3*fx¦ | 2247– 2740
¦fy – 4*fx¦ | 830 –1164
Transmission bandwidth for B8 in this CA combination can be lower than 5 MHz, According to the Way forward on 2UL inter-band CA MSD test configurations (R4-144031), Choose 5-MHz bandwidth with full RB for all carriers (if supported in a CA combination) to essentially comply with the Rel-8 UL configurations for REFSENS tests and approach the worst-case self-desensitization condition

## Slide 3: Background(2/2)
IMD study and MSD analysis for CA_B8+B41 2UL CA were discussed in [1-5]
[1]R4-160553, TP for TR 36.714-02-02 on operating bands, channel bandwidths per operating band and co-existence analysis for dual uplink of CA_8A-41A, CMCC
[2] R4-162202, MSD for 8+41 2UL CA, Huawei, HiSilicon
[3] R4-161884, MSD analysis for 2UL CA_8A_41A, MediaTek
[4] R4-163621, MSD for 8+41 2UL CA, Huawei, HiSilicon
[5] R4-164295, MSD analysis for 2UL CA_8A_41A , MediaTek

## Slide 4: Way forward
Only IMD5 is defined in the specification, and a note to 36.101 : B8 is also subject to IMD3
The test bandwidth need to follow the way forward on 2UL inter-band CA MSD test configurations(R4-144031). 5 MHz carrier bandwidth is chosen for B8 and 10 MHz is chosen for B41