## Slide 1: WF on antenna connection for legacy 2Rx tests on 4Rx bands
Document for: Discussion
Source: Ericsson, Samsung, Intel, Huawei
3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd-27th May 2016
Agenda Item: 6.6.1
R4-164743

## Slide 2: Existing Options for antenna connections
  Option 1: Connect 2 of the 4 Rx with data source from SS to perform 2Rx tests, depending on the UE’s declaration and AP configuration, keeping the same requirements as 2Rx tests.
  Option 2: Connect all 4 of the 4 Rx with data source from SS to perform 2Rx tests, keeping the same requirements as 2Rx tests.
  Option 3: Connect all 4 of the 4 Rx with data source from SS to perform 2Rx tests, with tighten requirement case by case.
  Option 4: For no interfering cell tests
    Pair two receiver antenna as one group and pair the other two as one group.
    The signal is generated and passed through faders in the same way as that for the tests based on 2 receiver antennas. Afterwards, a signal is split, duplicated and input to two receiver antenna belonging to the same pair.
    The 4 external noise signals with the level of NOC are statistically independent and input to 4 receiver antennas separately. pair two receiver antennas and connect the other 2 APs with the same inputs, i.e. AP 1 with the same input as AP 2 and AP 3 with the same input as AP4.
    Apply the 2Rx requirements with [XdB] lower SNR.
  Option 5: Test mode for any tests in 4Rx band

## Slide 3: Background
Agreements made in evening adhoc sessions from R4-164630 are the following.
  Outcome of RAN4#79 will be at least a CR capturing antenna connection for a testing UE on a 2RX band and a way forward should also capture the outcome of the discussion on testing on 4RX bands, even if that is that there is no conclusion.
Further discussions are needed during the meeting week in order to reach possible agreements on how to perform legacy 2Rx tests on any 4Rx bands.
In this WF a general solution to cover all legacy tests including tests with and without interfering cells is proposed for further study, with the purpose not to revisit each test to determine the margin, to be applied for demod/CSI requirements.
The XdB should be FFS.
  The study of determining XdB should be in the direction not to limit UE implementation of fall-back behaviours in all the test cases.
  XdB can be different between page 5 and page 6. Tests under interference scenario can be separately discussed.

## Slide 4: Option 4 proposed in R4-163392
2 Rx TESTING without interference
SS
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
UE
AP1
AP2
AP3
AP4
Splitter
Splitter

## Slide 5: Extended Option 4 with interfering cells
2 Rx (2x2)TESTING with interference
SS
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
UE
AP1
AP2
AP0
AP1
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
Splitter
Splitter
AP3
AP4
AP0
AP1

## Slide 6: General proposal 5 with attenuation without interference
SS
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
UE
AP1
AP2
AP3
AP4
Splitter
Splitter
Attenuation X dB
Atenuation X dB

## Slide 7: General proposal 5 with attenuation with interfering cells
SS
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
UE
AP1
AP2
AP0
AP1
Splitter
Splitter
Fader2
Fader1
Fader4
Fader3
Splitter
Attenuation X dB
Splitter
Attenuation X dB
AP3
AP4
AP0
AP1

## Slide 8: General proposal 6 with attenuation without interference
Notes:
  FFS on the value of X, and X dB could be 0dB
  FFS on the Y dB tightening requirements on top of legacy 2RX requirement for demodulation cases, and Y dB could be 0dB.

## Slide 9: Theoretical analysis with AWGN & ideal channel estimation

## Slide 10: Theoretical analysis with interference
If using splitter like page 6, covariance matrix is constructed with a pattern.
(RXAP0, RXAP1) and (RXAP3, RXAP4) is always correlated with a scalar alpha.

## Slide 11: Summary and proposals
Given perfect CE, the performance with new 4RX connection method (with power attenuation factor α2 ) applied will be equivalent to 2RX connection method with noise power attenuated by 1+α2
Then, the relationship btw. attenuation factor and SNR increased level:
On the other hand, the CE will be greatly degraded on attenuated two branches especially when attenuation factor is large, and then the introduced loss should be compensated by higher SNR level.
Further study and propose X dB for demod/CSI tests with and without interfering cell conditions for the future meetings.
Other proposals are not precluded.
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
SNR increase level in dB | 3.01 | 2.53 | 2.12 | 1.75 | 1.45 | 1.19 | 0.97 | 0.79 | 0.64 | 0.52 | 0.41