## Slide 1: 3GPP TSG-RAN WG4 Meeting #79 Nanjing, China, 23rd – 27th May, 2016
Intel, Samsung
Network-assisted signalling for high speed scenarios
R4-164764

## Slide 2: Background
Currently, RAN4 identified that legacy channel estimation and RRM measurement needs to be improved for HST support.
It is importance for a UE to accurately know about HST environments for enabling HST UE behaviours.
Intentions of signalling introduction are
  1. to prevent regular UEs from enabling HST UE behaviours
  2. to utilize effectively HST UE functions in HST running circumstances

## Slide 3: HST RRM
  Companies’ preferences on RRM signaling are provided in the next meeting.
  HST scenario indicator options :
      Option 1 : Use 1-bit HST indicator in common with HST UE demod
    Option 2 : reuse an existed signaling
    HST UE need only measure the cell in the limited neighbor cell list in HST. Neighbor cell list signaling options :
    Option 1 : Introduce a new signaling for HST neighbor cell list
    Option 2 : reuse existed signaling
Other signaling introduction or reuse for HST scenario indication is not precluded.

## Slide 4: HST Demod
  Companies’ preferences on HST demodulation signaling are provided in the next meeting.
  Possible Signallings :
  Signalling 1 : HST is running on HST rail at high speed ( Used in common with HST UE RRM )
  Signalling 2 : Signalling at location of changing SFN such as cell edge of SFN RRHs
  Signalling 3 : Unidirectional or Bidirectional SFN
Other signaling introduction or reuse is not precluded.

## Slide 5: Signaling method
HST signaling is cell specific.
HST UE tests are conducted with a given HST signaling, if a signaling is introduced.
HST UE performance robustness is FFS ( i.e. performances when HST CE is applied for low Doppler channels )
  HST UE needs blind detection for HST scenarios based on the signaling.