## Slide 1: Blind Detection Conclusions on MUST Case 3
MediaTek
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22nd -26th August 2016
Agenda Item: 8.19.2
R4-165134

## Slide 2: Way Forward
In CRS-based TMs,
  Interference existence detection is not feasible
    Performance degradation is observed in legacy SU-MIMO scenario due to non-zero blind detection error rate
  Given interference present, given interference existence signaled and practical detection algorithm, the degradation at 10% BLER of the ideal performance is summarized in the table in the next page

## Slide 3: Way Forward
 | Modulation combination {target, interference} | Throughput degradation at 90% throughput of ideal performance |  | 
 |  | Detecting precoder, signaling modulation | Detecting modulation, signaling precoder | Detecting both precoder and modulation
4TX | {QPSK, QPSK} | 2% | 2% | 4%
 | {QPSK, 16QAM} | 2% | 2% | 4%
 | {QPSK, 64QAM} | 2% | 2% | 4%
 | {16QAM, QPSK} | 16% | 5% | 25%
 | {16QAM, 16QAM} | 11% | 6% | 25%
 | {16QAM, 64QAM} | 11% | 7% | 19%
 | {64QAM, QPSK} | 60% | 21% | 76%
 | {64QAM, 16QAM} | 47% | 18% | 58%
 | {64QAM, 64QAM} | 47% | 13% | 56%
2TX | {QPSK, QPSK} | < 1% | 2% | 5%
 | {QPSK, 16QAM} | 1% | 3% | 5%
 | {QPSK, 64QAM} | < 1% | 3% | 5%
 | {16QAM, QPSK} | 12% | 5% | 23%
 | {16QAM, 16QAM} | 15% | 10% | 27%
 | {16QAM, 64QAM} | 20% | 15% | 31%
 | {64QAM, QPSK} | 32% | 26% | 59%
 | {64QAM, 16QAM} | 35% | 15% | 47%
 | {64QAM, 64QAM} | 43% | 18% | 49%

## Slide 4: Way Forward
In DMRS-based TMs, with practical detection algorithm, the degradation at 10% BLER of the throughput with ideal information is summarized below
 | Modulation combination {target, interference} | Throughput degradation at 90% throughput of ideal performance | 
 |  | Fully blind | With only modulation signaled
SU |  | <1% | 
MU | {QPSK, QPSK} | 6% | 4%
 | {QPSK, 16QAM} | 6% | 4%
 | {QPSK, 64QAM} | 7% | 4%
 | {16QAM, QPSK} | 15% | <1%
 | {16QAM, 16QAM} | 13% | <1%
 | {16QAM, 64QAM} | 14% | <1%
 | {64QAM, QPSK} | 33% | <1%
 | {64QAM, 16QAM} | 31% | <1%
 | {64QAM, 64QAM} | 26% | <1%