## Slide 1: 3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 Aug, 2016
Nokia, [Ericsson, Huawei, DoCoMo]
Way forward on NPRACH performance requirements
R4-166618

## Slide 2: Background
It is observed that significant gap exists between NPRACH detection performance and timing estimation performance.
  Ref: R4-164350, R4-164351
It is observed that cell-ID and signature have significant impact on NPRACH ToA estimation performance
  Ref: R4-79AH-0067
It is observed that total timing probability (joint probability of missed detection and error timing estimation) is higher than targets and it is channel dependent
  Ref: R4-166616

## Slide 3: Way Forward
The SNR for minimum performance shall be defined to satisfy
  Option 1: Missed detection probability <=1%, including: detecting different preamble than the one that was sent, not detecting a preamble at all, or detecting the correct preamble detection but with the wrong timing estimation.
  Option 2: Pmd<=1%, and Pte<=1%, where Pmd includes: detecting different preamble than the one that was sent, or not detecting a preamble at all.
  Other options are not excluded
Timing limit
  Option 1: 2.5us
  Option 2: 5us
  Other options are not excluded
Repetition number
  Greater or equal to 8
Cell-ID and signature
  fixed

## Slide 4: Updated Simulation assumptions
Parameter | Values
NPRACH preamble format | 0
Number of Repetitions | 2, 8, 32
Number of Subcarriers | 12
Antenna configuration | 1 x 2
Cell-ID | [0, random cell-ID 503, 447]
NPRACH signature | 0
Timing offset (us) | [30]
frequency offset | 0Hz (AWGN); [200Hz] EPA1
Propagation channels | AWGN, EPA1
Detection performance | Missed detection rate (1%) with false alarm rate (0.1%)
Timing estimation | Timing error probability with limits 2.5us, [5us]