## Slide 1: Way Forward on Testability
Intel Corporation
3GPP TSG-RAN WG4 Meeting #80 R4-166711
Gothenburg, Sweden, 22-26 August, 2016

## Slide 2: Background
Discussions on NR testability have progressed in RAN4
References:
TDoc # | Title | Source
R4-164984 | On the definition of RF conformance measurement reference points | ROHDE & SCHWARZ
R4-165050 | Testability considerations for NR | Intel Corporation
R4-165066 | Necessity of consideration of both requirements and testability | NTT DOCOMO INC, Anritsu
R4-165126 | Considerations on NR RRM testing | Ericsson
R4-165257 | On UE RF high frequency testability | Huawei, Hisilicon
R4-165772 | UE Conformance Testing for mmWave | Qualcomm Incorporated
R4-166056 | Discussion on the testability of NR | Huawei, HiSilicon
R4-165064 | Consideration on RAN4 NR SI work | NTT Docomo

## Slide 3: Agreements (1)
Below a certain frequency threshold, such as [6 GHz], the UE testing setup can be reused from LTE
General test methodology definition is needed for NR with the following aspects:
  For BS and UE
  Covering RF, RRM, Demodulation
For each aspect above, identify parameters which will require a testing setup
A study whether NR requirements can be tested with OTA based method or not is needed, capturing:
  Selected test methods and associated constraints
  Reasons why the test methods are feasible
  An evaluation of the consistency across the measured requirements with expected relationships (e.g. REFSENS and blocking, etc.)
The following potential recommendation to RAN Plenary, with the final decision to be confirmed during RAN #73, is suggested for further discussion:
  A new TR is needed as a container of NR testability agreements

## Slide 4: Agreements (2)
UE RF testability
  Potential testing setups need to be identified
  Further details of testing methodologies are FFS
UE RRM testability
  Potential testing setups and channel models need to be identified
  Evaluate if using IF is feasible
  Further details of testing methodologies are FFS
UE Demodulation testability
  Potential testing setups and channel models need to be identified
  Evaluate if using IF is feasible
  Study if a subset of tests that can be shifted to be tested at low frequency utilizing the legacy LTE test setup
  Identify areas of test that will be new to NR that may fall between traditional RRM and demod tests
  Further details of testing methodologies are FFS

## Slide 5: Agreements (3)
BS RF testability
  For EIRP and EIS, testing setup definition based on AAS specification [TS 37.145] as a baseline
  Further details of testing methodologies are FFS
BS RRM testability
  The purpose and scope of BS RRM testing approaches should be discussed
  Potential testing setups need to be identified
  Evaluate if using IF is feasible
  Further details of testing methodologies are FFS
BS Demodulation testability
  The purpose and scope of BS demodulation testing approaches should be discussed
  Potential testing setups to capture the scope need to be identified
  Evaluate if using IF is feasible
  Further details of testing methodologies are FFS