## Slide 1: WF on Rel-13 CRS-IM and DL Control Channel IM UE Capabilities
Intel Corporation, Huawei, HiSilicon, Qualcomm, Samsung
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 August 2016
Agenda Item: 5
R4-166737

## Slide 2: Rel-13 CRS-IM UE Capabilities
Background
  RAN4 has agreed on a per-UE CRS-IM capability signaling in Rel13. In RAN4 #77 discussion, it has been agreed as
    A new UE capability signaling will be introduced indicating CRS-IM capability on at least one CC, without the information of supported CCs, if the feature is not mandatory.
Non-TM10 CRS-IM UE capability
  UE capability signaling will be introduced indicating CRS-IM capability on at least one CC for up to N CC CA configuration. UE signals a single N value to indicate the max N CC CA configuration where UE may apply CRS-IM.
  Example
    N = 0 => UE does not support CRS-IM
    N = 1 => UE supports CRS-IM on a single carrier
    N = 2, 3, .. => UE supports CRS-IM on at least one CC for up to 2,3,… CC CA configurations. Note: UE may not perform CRS-IM on more than 1 CC.

## Slide 3: Rel-13 CCIM UE Capabilities
Background
  RAN4 #78 agreements (R4-161170)
    Two types of reference IM Receiver structures for PDCCH/PCFICH/PHICH in synchronous networks
      Type A IM receiver: LMMSE-IRC + CRS-IC
      Type B IM receiver: E-LMMSE-IRC + CRS-IC
    Define different UE capabilities for the two types of IM Receiver structures
      UE Capability #1: Support Type A IM receiver
      UE Capability #2: Support Type B IM receiver
  RAN4 #78bis agreements (R4-162757)
    Single UE capability should be defined for all DL control channels
    UE capabilities signaling is needed
    DL Control Channel IM receivers applicability

## Slide 4: Rel-13 CCIM UE Capabilities
Background (cont.)
  RAN4 #78bis agreements (R4-162757)
    Type A CCIM capability is the pre-requisite capability for Type B CCIM receiver capability. UEs with Type B CCIM receiver should support Type A CCIM processing.
    UE capabilities signaling will be introduced
      Option1:
        Bit #1: Support of Type A DL Control IM receiver capability
        Bit #2: Support of Type B DL Control IM receiver capability for PDCCH/PCFICH/PHICH receive processing in synchronous networks
      Option2:
        Bit #1: Support of generic Dl Control Channel IM capabilities. Depending on whether UE supports Type A/B processing it will pass different test cases to confirm the capability.
    Capability signaling method
      Option 1
        Per UE capability signaling. Signaling provided under assumption that UE supports feature on at least one CC. UE does not provide the information of supported CCs.
      Option 2
        Per CC capability signaling. Details FFS.

## Slide 5: Rel-13 CCIM UE Capabilities
DL Control Channel IM (CCIM) UE capabilities
  Per-UE capability signaling will be introduced indicating CCIM capability on at least one CC for up to N CC CA configuration.
  2-bit signaling is used to indicate support of Type A and Type B receivers capabilities
    Bit #1: Support of Type A DL Control IM receiver capability
    Bit #2: Support of Type B DL Control IM receiver capability for PDCCH/PCFICH/PHICH receive processing in synchronous networks
  UE signals a single N value to indicate the max N CC CA configuration where UE may apply CCIM (see example in Slide 2 for CRS-IM)
  In case capability signalling is provided, for the CA scenarios the CCIM is guaranteed to be supported on at least one component carrier