## Slide 1
3GPP TSG-RAN WG4 #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
Agenda item: 8.11.4
LG Electronics, Huawei, CATT
WF on way to close V2V RRM core requirement timely
R4-166755

## Slide 2: Way Forward
RAN4 agree to specify the minimum set of RRM core requirements based on RAN1 and RAN2 agreements for the corresponding minimum set of specifications in order to close the V2V RRM core part
RAN4 prioritize to specify the requirement for V2V stand-alone operating on a dedicated V2V carrier (e.g. Band 47) in this meeting
  No cellular control (no eNB-based synch for V2V, no resource control, no resource pool configuration etc)
  UE may be inside WAN coverage on another carrier
  Dedicated carrier has no WAN
  Dedicated TX and RX chains assumed for V2V operation on the dedicated carrier
RAN4 prioritize to specify the requirement related to GNSS as the only synchronization reference in this meeting
  No procedures and requirements will be defined for SLSS based synchronization. SLSS synchronization assumed to be not supported.
Other synchronization sources(e.g. eNB, SyncRef UE) to be specified in V2X WI.

## Slide 3: Way Forward
UE transmission timing
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    TA : NTA,SL =0
    TE : +/- 12 Ts

## Slide 4: Way Forward
Interruption
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    No interruption to LTE communication

## Slide 5: Way Forward
GNSS selection requirement
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    UE should use GNSS synchronization source in case it has sufficient reliability
      GNSS synchronization source is considered to have sufficient reliability in case
        option1 : it allows UE to satisfy the timing and frequency accuracy requirements. The side condition for GNSS signal so that the derived timing and frequency accuracy meet the requirements will not be specified.
        Option2 : GNSS meets the minimum signal level requirement [example] defined in TS36.171
        Other option are not precluded
    In case of unreliable GNSS synchronization source, no procedures will be defined.

## Slide 6: Way Forward
Initiation/Cease of SLSS transmissions
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    Not applicable. GNSS is the only synchronization source

## Slide 7: Way Forward
Measurement accuracy of S-RSRP
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    Not applicable. GNSS is the only synchronization source
      If found other use-case except for SyncRE UE selection/reselection and Initiation/Cease of SLSS transmission, it can be studied in next meeting.

## Slide 8: Way Forward
Cell identification
  For V2V stand-alone operating on a dedicated V2V carrier using GNSS as synchronization reference
    Not necessary

## Slide 9: Way Forward
Measurement for congestion control & collision avoidance
  RAN4 to define measurement requirements for congestion control and collision avoidance based on RAN1 agreements

## Slide 10: Way Forward
Offset to shift the DFN #0 w.r.t the reference timing derived from GNSS
  Ran4 to study RRM impact based on RAN1 agreement in next meeting