## Slide 1: Blind Detection Conclusions on MUST Case 3
MediaTek, ZTE
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22nd -26th August 2016
Agenda Item: 8.19.2
R4-166810

## Slide 2: Way Forward
In RAN4#80 meeting, RAN4 has discussed the blind detection on MUST Case 3 for both CRS and DMRS-based TMs. It is agreed to further investigate the blind detection performance particularly in the following aspects
  In DMRS-based TMs, performance and blind detection feasibility with interference on non-orthogonal DMRS ports
  Blind detection feasibility of different receiver types based on the different amount of available interference parameters
The throughput degradation at the SNR that achieves 10% BLER under ideal information is used as the metric for determining the feasibility of blind detection

## Slide 3: For Information Receiver Types
In CRS based-TMs, interference parameters to be studied are existence, precoder, modulation order
  R-ML receiver to be used when all parameters are signaled or detected
  Enhanced IRC receiver to be used when all parameters but modulation order are signaled or detected
  MRC to be used when none is signaled or detected
In DMRS based-TMs, interference parameters to be studied are existence and modulation order
  R-ML receiver to be used when all parameters are signaled or detected
  Enhanced IRC receiver to be used when only existence is signaled or detected
  IRC receiver to be used when none is signaled or detected

## Slide 4: For Information Simulation parameters
Parameter for target UE | Value
Bandwidth | 10MHz
Cyclic prefix | Normal
Propagation channel | EVA5, ETU5
Number of OFDM symbol for control region | 3
Subframes with PDSCH | #1, 2, 3, 4, 6, 7, 8 and 9
Number of PRBs of PDSCH | Baseline: 50
Rank | Baseline: 1
HARQ | Disabled
Number of PRB used for one decision | Baseline: 1 Options: 1 RBG, 1 subband, full band
Number of REs used in a PRB for blind detection | To be specified in the contribution
Detection algorithm | To be specified in the contribution
Channel/noise estimation | Non-ideal

## Slide 5: For Information Simulation Parameters
Parameter | Value | 
 | CRS-based TM | DMRS-based TM
Frame structure | FDD | TDD
Antenna configuration | 2x2 ULA low correlation 4x2 ULA low correlation | 4x2 ULA low correlation 8x2 Xpol high correlation
Cell-specific reference signals | Antenna ports 0,1 Antenna ports 0,1,2,3 | Antenna ports 0,1
Transmission mode | TM4 | TM9
Number of interference UEs | 1 | 1 with (i) OCC-2 or (ii) OCC-4
Resource allocation of interference UE | Full band | 
MCS of target UE | MCS#0, MCS#10 and MCS#17 | 
Modulation order of interference UE | QPSK, 16QAM and 64QAM | 
Precoding of target UE | Follow UE’s wideband PMI report with reporting mode 1-1 | 
Precoding of interference UE | Random with granularity of 1 PRB. Other options are not precluded. | 
TX EVM | 6% | 
Parameters to be blindly detected or signaled | existence, precoder, modulation order | existence (DMRS port) and modulation order