## Slide 1: Way forward on eAAS

## Slide 2: Observations on ACLR
ACLR defined as (Integrated power on the wanted assigned channel) / (Integrated power on the adjacent channel of the unwanted emissions) is verified by simulation to be a good metric for ensuring co-existence performance
  Integrated power refers to a suitable approximation to total radiated power allowing for realistic measurement with reasonable time
Further work is needed to verify that measurement is feasible and complexity is reasonable

## Slide 3: Decision on EVM
EVM for beams steered towards specific users has been discussed during the current and previous meetings and it was agreed that for these beams, EVM should be defined in the centre of the main lobe. The need or lack thereof of an EVM requirement for beams covering a cell was not discussed.
For user specific beams
  EVM defined in the centre of the main lobe
  EVM met with a beam steered anywhere within the EIRP accuracy directions set
  EVM tested with the same beam directions as EIRP accuracy
EVM requirement, if any, for non user specific beams TBC

## Slide 4: For further discussion/contribution (no decision; information & guidance for following meetings)
SEM
  Further discuss SEM values (need for declaring active transmitters etc.)
  Further discuss TRP for in band SEM
Reference sensitivity
  Clarify what is needed to decide whether to differentiate reference and minimum sensitivity and whether to rename the term reference sensitivity (or decide)
Minimum sensitivity method
Blocking
  Further discuss how to define the blocking level/direction(s) and test, considering complexities of statistical system simulation and a simple test method
  Further discuss whether throughput or some power or SINR measurement should be used as a metric, considering amongst other things uncertainty
  Further discuss how and where to determine the test pass criteria