## Slide 1: WF on eMTC CEMode B RLM test
Nokia, Qualcomm, Ericsson
R4-167030
3GPP TSG-RAN WG4 Meeting #80
Gothenburg, Sweden, 22 - 26 Aug, 2016
Agenda Item: 6.2.1.1

## Slide 2: Proposals for test setup
The combination of aggregation level and repetition (AL,R) used for the hypothetic MPDCCH transmission is
  Set 1: (24, 256) for Qout and (8,128) for Qin for OoS test cases
  Set 2: (16, 128) for Qout and (4,64) for Qin for IS test cases
  Note: the parameters can be revisited if major problem is identified during simulation.
Margins used to derive the SNR levels from Qin/out are to be decided in RAN4#80bis.
  Companies are encouraged to provide simulation results on Qin and Qout values for the two sets of combinations. Simulation assumptions are listed in next slide.

## Slide 3: MPDCCH simulation assumptions
Parameter | M-PDCCH (CE Mode B)
DCI format | DCI Format 6-1B
System Bandwidth | 10 MHz
Channel model | AWGN, ETU1, ETU5 and ETU30.
Antenna configuration | 2x1
Number of information bits (incl. 16 bits CRC) | 18
Antenna correlation | Low
Aggregation level and Repetition level | (24,256), (8,128), (16,128), (4,64)
Starting OFDM symbols (CFI) | 2
Frequency hopping | OFF
Number of PRB | 4 for Aggregation level = 4, 8, 16 2+4 for Aggregation level =24
Transmission type configured to UE | Distributed
DMRS scrambling sequence initialisation parameter for UE-SS | PCID = 1
Channel Estimation | DMRS based
UE residual frequency error | 50 Hz

## Slide 4: Proposals for test methodology
PUSCH is used to verify UE RLF status.
Detailed SNR variation and checking condition are described in next two slides as working assumption.
Companies are encouraged to study the details of the methodology. The methodology can be re-visited if any major problem is identified.

## Slide 5: Proposals for OoS
Test procedure
  Using one cell (Cell 1) in the OOS test. SNR variation of the Cell 1 is shown in figure below
  Time period T1: Connection setup with SNR1 (Qin + Margin)
  Point A: SNR is decreased from SNR1 to SNR2 (Qout + Margin)
    Time period T2: provide the UE with a UL grant for PUSCH transmission at Point B. The grant at is scheduled with [(24,256)] and the number of scheduling is FFS. UE should response to the UL grant. Point B allows UE to detect OoS and trigger RLF, but also allows UL transmission to finish before Point C.
  Point C: SNR is decreased from SNR2 to SNR3 (Qout - Margin)
    Time period T3: Allow UE to detect OOS and declare RLF (OOS timer disabled)
  Point D: SNR is increased from SNR3 to SNR1.
    Time period 4: provide the UE with a UL grant for PUSCH transmission at Point D. For a UE declared RLF before point D, it will not response to the UL grant. A UE that failed to declare RLF will stay in connection and response to the UL grant. The grant at is scheduled with [(24,128)]
OOS Test Requirements
  UE shall complete the UL transmission according to the UL grant during T2
  UE shall NOT response to the UL grant during T4
  The rate of correct events observed during repeated tests shall be at least 90%
T1
SNR1
SNR2
A
B
Qout
Qin
SNR3
C
D
T2
T3
T4
dT
dT
dT
E

## Slide 6: Proposals for IS
Test procedure
  Using one cell (Cell 1) in the IS test. SNR variation of the Cell 1 is shown in figure below
  Time period T1: Connection setup with SNR1 (Qin + Margin)
  Point A: SNR is decreased from SNR1 to SNR3 (Qout - Margin)
    Time period T2: Allow UE to detect OOS but has not triggered RLF, and allow UE to have enough time to get IS
  Point B: SNR is increased from SNR3 to SNR1.
    Time period 3: provide the UE with a UL grant for PUSCH transmission after Point C. Point C allows UE to detect OOS and trigger RLF
IS Test Requirements
  The UE shall transmit uplink signal according to the UL grant sent at Point B
  The rate of correct events observed during repeated tests shall be at least 90%
T1
SNR1
A
Qout
Qin
SNR3
B
C
T2
T3
dT
dT