## Slide 1: WF on Rel-13 DL Control Channel IM UE Capabilities
Intel Corporation, Huawei, HiSilicon, Qualcomm, Samsung
3GPP TSG-RAN WG4 Meeting #80 Gothenburg, Sweden, 22 - 26 August 2016
Agenda Item: 5
R4-167033

## Slide 2: Background (1)
RAN4 #78 agreements (R4-161170)
  Two types of reference IM Receiver structures for PDCCH/PCFICH/PHICH in synchronous networks
    Type A IM receiver: LMMSE-IRC + CRS-IC
    Type B IM receiver: E-LMMSE-IRC + CRS-IC
  Define different UE capabilities for the two types of IM Receiver structures
    UE Capability #1: Support Type A IM receiver
    UE Capability #2: Support Type B IM receiver
RAN4 #78bis agreements (R4-162757)
  Single UE capability should be defined for all DL control channels
  UE capabilities signaling is needed
  DL Control Channel IM receivers applicability

## Slide 3: Background (2)
RAN4 #78bis agreements (R4-162757)
  Type A CCIM capability is the pre-requisite capability for Type B CCIM receiver capability. UEs with Type B CCIM receiver should support Type A CCIM processing.
  UE capabilities signaling will be introduced
    Option1:
      Bit #1: Support of Type A DL Control IM receiver capability
      Bit #2: Support of Type B DL Control IM receiver capability for PDCCH/PCFICH/PHICH receive processing in synchronous networks
    Option2:
      Bit #1: Support of generic Dl Control Channel IM capabilities. Depending on whether UE supports Type A/B processing it will pass different test cases to confirm the capability.
  Capability signaling method
    Option 1
      Per UE capability signaling. Signaling provided under assumption that UE supports feature on at least one CC. UE does not provide the information of supported CCs.
    Option 2
      Per CC capability signaling. Details FFS.

## Slide 4: WF on Rel-13 CCIM UE Capabilities
Per-UE capability signaling needs to be introduced to indicate CCIM capability on at least one CC for up to N CC CA configuration:
  2-bit signaling to indicate support of Type A and Type B receivers capabilities
    Bit #1: Support of Type A DL Control IM receiver capability
    Bit #2: Support of Type B DL Control IM receiver capability for PDCCH/PCFICH/PHICH receive processing in synchronous networks
  N value signalling to indicate the max N CC CA configuration where UE may apply CCIM. Example
    N = 1 => UE supports CCIM on a single carrier
    N = 2, 3, .. => UE supports CCIM on at least one CC for up to 2,3,… CC CA configurations. Note: UE may not perform CCIM on more than 1 CC.
  For the CA scenarios the CCIM is guaranteed to be supported on at least one arbitrary CC.