## Slide 1: WF on MCL Relaxation for New Power Class for enhanced NB-IOT
u-blox, Neul, Huawei, HiSilicon, Vodafone, Nokia, Ericsson, Deutsche Telekom, ASTRI
R4-167174
3GPP TSG RAN WG4 #80
Gothenburg, Sweden, 22nd -26th August, 2016
Agenda item 8.23.1

## Slide 2: Background
New power class(es) has been specified as one of the enhancements feature for Rel-14 enhanced NB-IoT.
  New Power Class(es)
  Evaluate and, if appropriate, specify new UE power class(es) (e.g. 14dBm), and any necessary signaling support, to support lower maximum transmit power suitable for small form-factor batteries, with appropriate MCL relaxations compared to Rel-13 (RAN4, RAN2)
In RAN4#80, several companies identified the need for a lower power class UE for e.g. small form-factor devices, in addition, corresponding MCL relaxation was discussed for certain type of applications.

## Slide 3: Proposal 1
A reduction in maximum coupling loss shall be applied for UEs that adopt the lower transmit power class.
  Companies are invited to evaluate the appropriate maximum output power for the new power class with MCL relaxation as compared to 164dB MCL.
      For example: 164 - (23 - P) dB, whereas the reduction in MCL is (23-P), whereas P is the maximum transmission power of the new UE power class
      The group will evaluate for example P = 14dBm as a starting point