## Slide 1
3GPP TSG-RAN WG4 #80 R4-167193
August 22nd ‒ 26th, 2016
Gothenburg, SE
Agenda item: 8.18.2.1
Document for: Approval
Way Forward on UE Tx requirements for eLAA
Qualcomm Incorporated

## Slide 2: Way Forward
Agreements
  Max output power = [20] dBm (for purpose of MPR simulations)
    Further investigation to evaluate compliance with PSD limit
  ACLR1 = 30 dB
  General SEM: [Reuse LTE general SEM] (for purpose of MPR simulations)
  Spurious emissions: Reuse LTE spurious emissions
    Extend upper frequency range to 26 GHz (per ITU-R SM.329)
  EVM: Reuse LTE EVM
To be studied for next meeting
  MPR for general emission requirements
    May not reflect in-band emission depending on agreement of the requirement
    QPSK, 16QAM, 64QAM initially, 256QAM to be addressed later
  Additional spurious emissions
    To include ETSI SEM, other regional SEM, ACLR2=40dB
    A-MPR for additional spurious emissions

## Slide 3: References
R4-165237, "ACLR for eLAA UEs" (NTT DOCOMO, INC.). (other)
R4-165409, "eLAA PA model" (Nokia). (other)
R4-166176, "Discussion on Power Spectral Density of UL transmissions in eLAA" (BROADCOM LIMITED). (discussion)
R4-166499, "General UE Tx requirements for eLAA in Band 46" (Qualcomm Incorporated). (discussion)
R4-166500, "eLAA UE MPR" (Qualcomm Incorporated). (discussion)
R4-166538, "UE unwanted emission mask in Rel-14 eLAA" (Ericsson). (other)
R4-166539, "CR on UE unwanted emission mask in Rel-14 eLAA" (Ericsson). (CR)