## Slide 1: WF on measurement gap enhancement
Intel, Nokia
3GPP TSG-RAN WG4 Meeting #80bis R4-167265
Ljubljana, Slovenija, 10th – 14th October 2016

## Slide 2: Shorter MGL for synchronous operations
Two Shorter MGL based gap pattern configurations are introduced
  MGL=3ms
  MGRP: 40ms and 80ms

## Slide 3: Shorter MGL for synchronous operations
Table 8.1.2.1-1: Gap Pattern Configurations supported by the UE can be updated as
Gap Pattern Id | Measurement Gap Length (MGL, ms) | Measurement Gap Repetition Period (MGRP, ms) | Minimum available time for inter-frequency and inter-RAT measurements during 480ms period (Tinter1, ms) | Measurement Purpose
0 | 6 | 40 | 60 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
1 | 6 | 80 | 30 | Inter-Frequency E-UTRAN FDD and TDD, UTRAN FDD, GERAN, LCR TDD, HRPD, CDMA2000 1x
2 | 3 | 40 | 24 | Inter-Frequency E-UTRAN FDD and TDD for cells with time difference according to section TBD
3 | 3 | 80 | 12 | Inter-Frequency E-UTRAN FDD and TDD for cells with time difference according to section TBD

## Slide 4: Per CC measurement gaps
It is FFS on how to capture the case when no measurement gap is configured on CC.
Decision on new gap pattern is made in RAN4#81
  Non-uniform gap pattern
  Uniform gap pattern with MGRP>80ms
Companies are encouraged to provide input on how to capture parallel measurement requirements