## Slide 1: WF on IRC tests for 4Rx CA WI
Ericsson, QC
3GPP TSG-RAN WG4 Meeting #80bis Ljubljana, Slovenia, 10th-14th Oct, 2016
Agenda Item: 8.30.3.2
R4-168704

## Slide 2: Background
It was agreed in the adhoc minutes for IRC tests to have a WF to capture the following
  Different options on defining the tests
    Option 1: Check CA configs on possibility to reuse 10MHz test only for multiple CA configs
    Option 2: Take maximum aggregated bw reusing same methodology as Rel-12 CA tests
  TM: TM6/TM4[/TM4], TM9/TM9[/TM9]
  Number of CCs to be supported by IRC CA is FFS
    2Rx
    4Rx
In this WF more details are provided for further investigations for future meetings

## Slide 3: Test structure Option 1
Reuse 10MHz IRC tests with 2Rx and/or 4Rx as single carrier test requirements to be applied to CA configs that support BW combinations with 10MHz on at least 2 CCs.
Check how many CA configs among all CA configs fulfills such BW combinations.
Further study the applicability rule based on that.

## Slide 4: Test structure Option 2
Reuse the same methodology from Rel-12 of applying single carrier requirement to CA on all possible maximum aggregated BW with requirements for either 2Rx IRC or 4Rx IRC depending on if it’s 2Rx or 4Rx CC.
Further study the applicability rule based on that.

## Slide 5: TM for IRC CA
Introduce 2 tests with TMs as following
  2Rx tests:
    TM6 for serving cell with TM4 on 2 interfering cells
    TM9 for serving cell with TM9 on 2 interfering cells
  4Rx tests
    TM6 for serving cell with TM4 on 1 interfering cell
    TM9 for serving cell with TM9 on 1 interfering cell

## Slide 6: Number of CCs supported by IRC+CA
It’s FFS for the number of CCs supported by IRC+CA. The following options can be considered for further evaluations and other options are not precluded.
  Option 1: Same maximum number of CCs up to 5 are supported with test structure Option 2.
  Option 2: Limited number of CCs e.g. 2 CCs are supported with either test structure Option 1 or 2.
  Option 3: Different number of CCs are supported regarding the tests are performed on 2Rx or 4Rx.
Companies are encouraged to bring more inputs on this together with considerations on the test structure and applicability rules