## Slide 1: 3GPP TSG-RAN WG4 Meeting #80Bis Ljubljana, Slovenia, 10-14, October, 2016
Huawei,HiSilicon…
Way forward on NB-IoT transmission signal pattern for NPDSCH demodulation performance
R4-168798

## Slide 2: Background
During RAN4#80, WF R4-167075 about NPDSCH transmission pattern was agreed with the following options:
  Option 1: Use different Noc levels for NPDCCH and NPDSCH
    For the details see the next pages
  Option 2: Use larger repetitions for NPDCCH and keep Noc level constant in the whole test
  Option 3: Other options are not precluded
During RAN4#80Bis, R4-167571 gave a compromised proposal of Option 1 and Option 2.

## Slide 3: NPDSCH case
For the compromised method of Option 1 and Option 2, the general consideration is to use short NPDCCH repetitions and decide the Noc level for NPDCCH as per NPDSCH case:
  Set NPDCCH to certain repetition number, e.g. 8, and find the minimum SNR to achieve [1%] NPDCCH mis-detection;
  Find the “SNR gap” between the NPDCCH with repetition number [8] and each NPDSCH case;
  Set -93dBm/15kHz for Noc in NPDSCH subframe;
  Set [-93dBm-(SNR gap)]dBm/15kHz for Noc level in NPDCCH subframe;
  Apply [6dB]power boosting for NPDCCH; compared to CRS
  Add a certain margin [5]dB on the Noc level for NPDCCH
We give an specific example in the following slides.

## Slide 4: Appendix: NPDSCH case 1
  SNR at repetition number 1 for NPDCCH: 8.3dB
  SNR for NPDSCH case 1: 3.0dB
  SNR gap between NPDCCH and NPDSCH: 5.3dB
Set -93dBm/15kHz for Noc in NPDSCH subframe;
Set [-98.3]dBm/15kHz for Noc level in NPDCCH subframe
Apply [6dB]power boosting for NPDCCH;
  Add a certain margin [5]dB on the Noc level for NPDCCH, then Noc for NPDCCH is -103.3dBm/15kHz

## Slide 5: Appendix: NPDSCH case 2
  SNR at repetition number 8 for NPDCCH: 1.4dB
  SNR for NPDSCH case 1: -8.0dB
  SNR gap between NPDCCH and NPDSCH about: 10dB
Set -93dBm/15kHz for Noc in NPDSCH subframe;
Set [-103]dBm/15kHz for Noc level in NPDCCH subframe
Apply [6dB]power boosting for NPDCCH;
  Add a certain margin [5]dB on the Noc level for NPDCCH, then Noc for NPDCCH is -108dBm/15kHz

## Slide 6: Appendix: NPDSCH case 3
  SNR at repetition number 8 for NPDCCH: 1.4dB
  SNR for NPDSCH case 1: -13.3dB
  SNR gap between NPDCCH and NPDSCH about: 15dB
Set -93dBm/15kHz for Noc in NPDSCH subframe;
Set [-108]dBm/15kHz for Noc level in NPDCCH subframe
Apply [6dB]power boosting for NPDCCH;
  Add a certain margin [5]dB on the Noc level for NPDCCH, then Noc for NPDCCH is -113dBm/15kHz

## Slide 7: Appendix: NPDSCH case 4
  SNR at repetition number 8 for NPDCCH: 7.4dB
  SNR for NPDSCH case 1: -6.7dB
  SNR gap between NPDCCH and NPDSCH about: 14dB
Set -93dBm/15kHz for Noc in NPDSCH subframe;
Set [-107]dBm/15kHz for Noc level in NPDCCH subframe
Apply [6dB]power boosting for NPDCCH;
  Add a certain margin [5]dB on the Noc level for NPDCCH, then Noc for NPDCCH is -112dBm/15kHz

## Slide 8: Appendix: NPDSCH case 5
  SNR at repetition number 8 for NPDCCH: 6.2dB
  SNR for NPDSCH case 1: -13.4dB
  SNR gap between NPDCCH and NPDSCH about: 20dB
Set -93dBm/15kHz for Noc in NPDSCH subframe;
Set [-113]dBm/15kHz for Noc level in NPDCCH subframe
Apply [6dB]power boosting for NPDCCH;
  Add a certain margin [5]dB on the Noc level for NPDCCH, then Noc for NPDCCH is -118dBm/15kHz