## Slide 1: Way Forward on NB-IoT UE Uplink Timing Error
Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, […]
R4-168790
3GPP TSG-RAN WG4 #80
Ljubljana, SI, 10 - 14 Oct 2016

## Slide 2: Background
NB-IoT UE UL Tx timing errors is currently defined as [80Ts] in TS 36.133 [1].
Very large Tx timing errors may only take place under very low SNR level, such as NRS Ês/Iot = -15 dB
Defining UL Tx timing errors with [80Ts] only without considering side condition may mislead UE’s design with target Tx timing errors of [80Ts] even under better side conditions
Since NP80Ts equals to CP/2, UE UL Tx timing errors of [80Ts] when combining with other timing errors will cause NPUSCH timing error out of the CP window
The impact of large UL Tx timing errors exceeding the CP window were investigated in RAN4#80bis (see, e.g., R4-167876, R4-168736). Initial link level simulation results show that there might be large impact on NPUSCH performance when the UL Tx timing errors exceeding the CP window

## Slide 3: Background
When UL Tx timing errors exceeding the CP window, it will also cause inter symbol interference as illustrated in the following figure. The impact will be presented regardless the number of transmission tones, including single-tone case.
UE1
CP
UE2
CP
Case 1: Perfect NPUSCH timing
UE1
CP
UE2
CP
Case 2: NPUSCH timing error < CP
Case 3: NPUSCH timing error > CP
UE1
CP
UE2
CP
CP Window
Time window with valid data samples
inter symbol interferences
Reduction of valid data samples due to ISI

## Slide 4: Agreements
Clarify that NB-IoT UE UL Tx timing error requirement of [80]Ts is applicable under side condition NRS Ês/Iot  -15 dB in TS 36.133
Add additional NB-IoT UE UL Tx timing error requirement of [TBD Ts] applicable under side condition NRS Ês/Iot  -6 dB in TS 36.133
The [TBD Ts] will be determined in future RAN4 meetings RAN4#81.
The impact of transmission of using different-tones (1,3,6 and 12) are to be further studied till next meeting.