## Slide 1
3GPP TSG-RAN WG4 #80bis R4-168820
October 10th ‒ 14th, 2016
Ljubljana, SI
Agenda item: 8.18.2
Document for: Approval
Way Forward on eLAA Tx requirements
Qualcomm Incorporated, Ericsson, Nokia, Skyworks, …

## Slide 2: Way Forward (1/4)
General requirements (NS_01)
  Maximum output power
    23 dBm (class 3)
    Tolerance is +2/-2 or +2/-2.5. Companies to provide proposals with technical justification next meeting.
  Spectrum emission mask
    Use the E-UTRA general SEM
  ACLR1 = 30 dB
    UTRA ACLR not applicable in Band 46
  Transmit signal quality
    Test waveforms as proposed in R4-167987 but with the image measurement shifted by 1 RB to avoid IM and image overlap.
    Requirement for in-band emission not yet agreed, but companies shall assess the impact, if any, of in-band emissions to MPR

## Slide 3: Way Forward (2/4)
Regional requirements (NS other than NS_01)
  NS for Japan
    To include ACLR2 = 40 dB, PSD = 10 dBm/MHz, and Japan-specific emission requirements
  NS for Region 1
    ETSI mask, PSD = 10 dBm/MHz
  NS for Region 2
    FCC emission requirements, PSD = 11 dBm/MHz in UNII-1 and UNII-2
  Companies to provide technical justification on the need for NS to indicate IEEE SEM
  Companies to verify the emission limits provided in R4-168591
  Companies to provide technical justification for other NS’s for other countries

## Slide 4: Way Forward (3/4)
Simulation assumptions
  PA size calibrated in the conventional manner with class 3 MOP, LTE waveform, E-UTRA ACLR, UTRA ACLR, general SEM
  QPSK, 16QAM, 64QAM modulations. 256QAM deferred for the time being.
  0 dBi antenna
  eLAA waveforms: At least a representative set of all possible eLAA waveforms.
Companies to provide simulations and MPR and A-MPR proposals for next meeting

## Slide 5: Way Forward (4/4)
Power control
  Proposal in R4-167988 to extend PC gap from 20ms to 40 ms, but maintain existing requirement.
  Companies to check for feasibility
Transient period delay
  Proposal in R4-167987 to extend the “off” time by t0 before the “on” transient period starts for a PUSCH or SRS transmission that starts after a gap. Transient period remains at 20 us.
  Companies to confirm that this proposal can be agreed.
LBT
  Proposal in R4-168592 for detection timing of 25us
  Companies to confirm that this proposal can be agreed