## Slide 1: WF on the OTA EVM for eAAS
NEC, Huawei, Ericsson
3GPP TSG-RAN WG4 Meeting #80bis R4-168873
2016Ljubljana, Slovenia, 10 – 14 October, 2016

## Slide 2: Background
RAN4 has discussed OTA EVM requirements for AAS BS for previous meetings. In RAN4#80 a Way Forward [1] was agreed.
  EVM requirement for user specific beams was agreed to be defined in the centre of the main lobe.
At this meeting a number of contributions [2,3,4,5] submitted with proposals addressing non-user specific beams.
Following the discussion in AAS evening adhoc, concept for specifying EVM for eAAS is converging and this Way forward captured the direction for agreement on OTA EVM requirements for eAAS.

## Slide 3: Way Forward
After RAN4#80bis, the agreed WF is as follows:
Manufacturer declares the intended EVM directions range.
The BS shall meet the OTA EVM requirement across the declared EVM directions range.
Conformance to OTA EVM requirements shall be demonstrated at the extreme directions of the declared coverage direction range and at the centre.
f
Q
Declared OTA EVM directions range
Centre of the EVM directions range
OTA EVM requirement conformance points
The following issues remain open for further discussion and decision:
  Whether OTA EVM requirements apply per beam or over the declared EVM directions range with only 1 EVM directions range.
  How to declare the coverage direction range, either adopting same as EIRP direction set or as a new EVM direction set, or something else, is still FFS.
  How to apply EVM requirements for AAS with multiple transceivers but without the ability to user beam steer is FFS.

## Slide 4: References
[1] R4-166930, WF clarifying open technical questions on AAS, Ericsson
[2] R4-168476, EVM Requirement considerations for eAAS, Ericsson
[3] R4-168423, EVM for non user beam steering systems, Huawei
[4] R4-168559, OTA EVM of AAS base station transmitters, Nokia, Alcatel-Lucent Shanghai Bell
[5] R4-168588, OTA EVM requirement for AAS, NEC