## Slide 1: Way forward on NB-IoT UE demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #80BIS
Ljubljana, Slovenia, 10-14, October, 2016
R4-168936

## Slide 2: NPDCCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 1% BLER in each case (Case 1&3 at SNR of -6dB, Case 2&4 at SNR of -12dB) from each contribution.
 | Case1 EPA5 2x1 low | Case2 ETU1 2x1 low | Case3 EPA5 1x1 | Case4 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [64] | [512] | [128] | [512, 1024]
Ericsson[R4-168208] | 128 | 1024 | 128 | 1024
Intel[R4-167243] | 128 | 1024 | 128 | 1024
CATT[R4-167506] | 128 | 1024 | 128 | 1024
Huawei[R4-167568] | 64 | 512 | 128 | 1024
Qualcomm[R4-168040] | 64 | 512 | 128 | 1024
ZTE[R4-168157] | 64 | 512 | 128 | 512
Nokia[R4-168740] | 64 | 512 | 64 | 512
Samsung[R4-168148] | 64 | 512 | 128 | TBD

## Slide 3: NPDSCH demodulation requirements
The below is a summary of the proposed number of repetitions to satisfy 70% of Max throughput around the targeted SNR.
 | Case2 EPA5 2x1 low | Case3 ETU1 2x1 low | Case4 EPA5 2x1 low | Case5 ETU1 1x1
RAN4#80 Assumption [R4-166656] | [16] | [192, 128, 256] | [32] | [192, 128, 256]
Intel[R4-167244] | 32 | 256 | TBD | 192
CATT[R4-167507] | 32 | 256 | 64 | 256
Huawei[R4-167569] | 16 | 256 | 32 | 256
Qualcomm[R4-168041] | 32 | 256 | 32 | 256
ZTE[R4-168158] | 16 | 128 | 32 | 128
Ericsson[R4-168209] | 32 | 256 | 32 | 192
Nokia[R4-168367] | 16/32 | 256/384 | 32 | 192/256
Samsung[R4-168148] | 32 | 256 | 32 | 256

## Slide 4: Agreements
Repetition numbers for NPDCCH demodulation requirements
Repetition numbers for NPDSCH demodulation requirements
Test case | Case 1 EPA5 2x1 | Case 2 ETU1 2x1 | Case 3 EPA5 1x1 | Case 4 ETU1 1x1
Repetition | 64 | 512 | 128 | 1024
Test case | Case 2 EPA5 2x1 | Case 3 ETU1 2x1 | Case 4 EPA5 1x1 | Case 5 ETU1 1x1
Repetition | 32 | 256 | 32 | 256

## Slide 5: Way forward
Interested companies are encouraged to provide the results with impairments for NPDCCH and NPDSCH demodulation requirements by RAN4#81.
Demodulation performance requirements will be derived from the values averaged from the results with impairments provided by companies
  DC subcarrier leakage should be considered when companies provide their results with impairments.
On top of the averaged value, the common margins due to result’s span will be added:
  NPBCH/NPDCCH: [0.3]dB
  NPDSCH: [0.5]dB
  RAN4#81 will decide the margin due to the result’s span for each test case.
    The above text is informative.