## Slide 1: Way Forward on NR UE Testability
Intel Corporation, CATR, Rohde & Schwarz
3GPP TSG-RAN WG4 Meeting #81 R4-1609162
Reno, USA, 14-18 November, 2016

## Slide 2: Background
Further agreements on UE RF parameters and discussions on testability have progressed the UE RF testability work in the NR study item

## Slide 3: Way Forward
Companies are encouraged to evaluate the following proposals by the next meeting
Baseline testing setup for UE TX and RX requirements
  Option 1: Far-field anechoic chamber setup with either conical cut or great circle test method is considered to be the baseline configuration
  Option 2: Far-field anechoic chamber setup with dual-axis positioning of the DUT is considered to be the baseline configuration
  Other options are not precluded
    Optimizations or alternate test methods are not precluded, provided equivalence of the measured metric can be demonstrated
  Whether the link antenna requires separate positioning control needs to be evaluated
The testing setup for each TX and RX RF parameter may utilize all or a subset of the components in the baseline testing setup
  A measurement link budget for the testing setup used to measure each TX and RX RF parameter is needed by the end of this study item
Measurement uncertainty element descriptions will be derived from the baseline testing setup once it is agreed

## Slide 4: Open issues
A further level of detail is needed
  Test setup descriptions
  Test setup dimensions
  Potential restrictions on the DUT (such as size, positioning, etc.)
  High-level descriptions of sources of measurement uncertainty
Clear definitions for abbreviations and terminology are needed