## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei
Way forward on eLAA demodulation performance
R4-1609424

## Slide 2: Background
As per the agreed WID RP-161832, the eLAA core part is complete and corresponding possible UE and BS demodulation performance requirements need to be defined.

## Slide 3: Test setup
Only PUSCH demodulation performance requirements to be defined with following configurations:
  Bandwidth: 20MHz
  Tx Antenna: 1Tx and 2Tx
  Rx Antenna: 2, 4 and 8
  Reference receiver: MMSE-IRC
  Propagation: EPA5 Low
  MCS: 16QAM 3/4 and 16QAM 5/6
  Starting PUSCH symbol configuration: 25us “01”
  Ending symbol configuration: second to last “1”
  Resource allocation: 011110 (30 = 10*(4-1) +0, i.e. RBstart = 0, and L = 4, total 4 interlaces allocated)
  Multiple consecutive subframes scheduling by using DCI format 0B/4B

## Slide 4: UL burst transmission model
Option 1: Use the UL grant of one licensed cell to schedule LAA SCell PUSCH, then the DL LBT procedure is not needed and UE(TE) only needs to do the normal UL Cat.4 LBT procedure for PUSCH transmission as per the received UL grant.
Option 2: Use the existing DL LBT model and configure “UL duration and offset” in the DCI to allow UE to use Channel access Type 2 for UL burst transmission.

## Slide 5: 10MHz BW LAA test
No performance requirements for LAA 10MHz bandwidth to be defined