## Slide 1: Simulation assumptions for SI acquisition for NB-IoT
Ericsson
3GPP TSG-RAN WG4 Meeting #81
Reno, Nevada, USA, 14-18, November, 2016
Agenda item: 5.6.4
R4-1609679

## Slide 2: MIB-NB/SIB1-NB/SIB2-NB acquisition
MIB-NB TTI = 640ms
SIB1-NB TTI = 2560ms
SIB2-NB TTI is up to eNB scheduling
Candidate algorithms to acquire MIB-NB/SIB1-NB/SIB2-NB
  Baseline: The “keep trying” decoder is definition is: The decoder simply “keeps trying” to decode the transmitted NPBCH frames until the decoder eventually gets lucky and decodes it correctly. With this solution there is a trade-off between coverage gain and decoding time (i.e. the number of decoding attempts). [Refer to R1-132908]
  Other algorithms are not precluded
MIB-NB/SIB1-NB/SIB2-NB acquisition delay = [90/99]%-ile of the number of frames required to successfully decode the MIB-NB/SIB1-NB/SIB2-NB
To obtain MIB-NB/SIB1-NB/SIB2-NB acquisition delay, companies are encouraged to provide CDF of MIB-NB/SIB1-NB/SIB2-NB acquisition time based on the simulation results in the following slides
All the impairment margin such as DC leakage should be considered

## Slide 3: Simulation assumption for MIB-NB acquisition in RRM core requirements under normal coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Number of NRS ports {1,2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
Modulation | QPSK | QPSK | QPSK | QPSK
Coding rate | 50/1600 | 50/1600 | 50/1600 | 50/1600
Payload (without CRC) | 34 bits | 34 bits | 34 bits | 34 bits
Target SNRs | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB

## Slide 4: Simulation assumption for MIB-NB acquisition in RRM core requirements under enhanced coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Number of NRS ports {1,2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
Modulation | QPSK | QPSK | QPSK | QPSK
Coding rate | 50/1600 | 50/1600 | 50/1600 | 50/1600
Payload (without CRC) | 34 bits | 34 bits | 34 bits | 34 bits
Target SNRs | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB

## Slide 5: Simulation assumption for SIB1-NB acquisition in RRM test under normal coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Deployment mode | In-band | In-band | In-band | In-band
Number of NRS ports {1, 2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
I_TBS {0/3/6/9} = {208/328/440/680bits} | 208bits | 208bits | 208bits | 208bits
Repetition number {4 ,8, 16} | 4 | 4 | 4 | 4
Target SNRs | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB

## Slide 6: Simulation assumption for SIB1-NB acquisition in RRM test under enhanced coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Deployment mode | In-band | In-band | In-band | In-band
Number of NRS ports {1, 2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
I_TBS {0/3/6/9} = {208/328/440/680bits} | 208bits | 208bits | 208bits | 208bits
Repetition number {4 ,8, 16} | 16 | 16 | 16 | 16
Target SNRs | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB

## Slide 7: Simulation assumption for SIB2-NB acquisition in RRM test under normal coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Deployment mode | In-band | In-band | In-band | In-band
Number of NRS ports {1, 2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
TBS (si-TB-r13) | [680]bits | [680]bits | [680]bits | [680]bits
Number of SF {1,2,…,8,10} | [10]8 | [10]8 | [10]8 | [10]8
NPDSCH Repetition number (*1) Si-WindowLength | [32][160] | [32][160] | [32][160] | [32][160]
Si-RepetitionPattern | every2ndRF | every2ndRF | every2ndRF | every2ndRF
NPDCCH Repetition number (*1) | [128] | [128] | [64] | [64]
Target SNRs | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB | -6 dB/ -4dB
(*1) The values are set based on R4-168791.

## Slide 8: Simulation assumption for SIB2-NB acquisition in RRM test under enhanced coverage
 | Case 1 | Case 2 | Case 3 | Case 4
Deployment mode | In-band | In-band | In-band | In-band
Number of NRS ports {1, 2} | 1 | 1 | 2 | 2
Propagation channel | EPA1 | ETU1 | EPA1 | ETU1
TBS (si-TB-r13) | [680]bits | [680]bits | [680]bits | [680]bits
Number of SF {1,2,…,8,10} | [10]8 | [10]8 | [10]8 | [10]8
NPDSCH Repetition number (*1) Si-WindowLength | [256][960] | [256][960] | [256][960] | [256][960]
Si-RepetitionPattern | every2ndRF | every2ndRF | every2ndRF | every2ndRF
NPDCCH Repetition number (*1) | [1024] | [1024] | [512] | [512]
Target SNRs | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB | -15 dB / -12dB
(*1) The values are set based on R4-168791.