## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei, [Nokia], [Ericsson], [ZTE], [Samsung]
Way forward on NB-IoT BS demodulation performance
R4-161xxxx

## Slide 2: Background
During RAN4#80bis meeting, WF R4-168720 about NB-IoT BS demodulation performance was approved.
How to define the final NB-IoT BS demodulation performances need to be finalized in RAN4#81.

## Slide 3: NPRACH
Case | Huawei | Ericsson | Samsung | Nokia | STD | SPAN | AVE
AWGN rep 8 | -6.4 | -6.2 | -4.5 | -4.3 | 1.1 | 2.2 | -5.4
AWGN rep32 | -10.7 | -10.9 | -9.0 | -9.27 | 1.0 | 1.9 | -10.0
EPA1 rep 8 | 2.4 | 2.5 | 3.0 | 4.4 | 0.9 | 1.9 | 3.1
EPA1 rep32 | -2.9 | -2.4 | -2.1 | -1.5 | 0.6 | 1.4 | -2.2
Ideal Simulation results: the results are aligned well
Practical Simulation results:
Case | Huawei | Ericsson | Samsung | Nokia | STD | SPAN | AVE | Ref. SNR
AWGN rep 8 | -4.9 | -4.2 | -2.5 | -1.3 | 1.6 | 3.6 | -3.2 | -3.2
AWGN rep32 | -9.2 | -8.9 | -7.0 | -6.3 | 1.4 | 2.9 | -7.8 | -7.8
EPA1 rep 8 | 3.9 | 4.5 | 5.0 | 7.4 | 1.5 | 3.5 | 5.2 | 5.2
EPA1 rep32 | -1.4 | -0.4 | -0.1 | 1.5 | 1.2 | 2.9 | -0.1 | -0.1
Final NPRACH performance requirement can be set as per the above averaged practical simulation results

## Slide 4: NPUSCH format 1:Ideal results - 1
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE
3.75KHz rep1 | -4.1 | -4.5 | -4.0 | -4.0 |  | 0.2 | 0.5 | -4.1
3.75KHz rep16 | -13.2 | -12.2 | -13.2 | -11.2 |  | 1.0 | 2.0 | -12.5
3.75KHz rep64 | -17.0 | -15.9 | -16.8 | -13.9 |  | 1.4 | 3.1 | -15.9
15KHz single rep1 | -4.1 | -4.1 | -4.1 | -4.6 | -4.1 | 0.2 | 0.5 | -4.2
15KHz single rep16 | -12.1 | -11.5 | -11.6 | -12.0 | -10.9 | 0.5 | 1.2 | -11.6
15KHz single rep64 | -16.5 | -15.1 | -15.5 | -15.7 | -15.0 | 0.6 | 1.5 | -15.6
Ideal Simulation results: the results are aligned well

## Slide 5: NPUSCH format 1: Ideal results - 2
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE
15KHz multi-tone12 rep2 | -0.9 | -1.7 | -2.6 | -2.3 | -0.9 | 0.8 | 1.7 | -1.7
15KHz multi-tone12 rep16 | -8.4 | -8.1 | -10.5 | -10.7 | -9.4 | 1.2 | 2.5 | -9.4
15KHz multi-tone12 rep64 | -12.1 | -12.1 | -14.4 | -14.7 | -14.0 | 1.3 | 2.6 | -13.5
15KHz multi-tone6 rep2 | -2.5 | -2.6 | -3.5 | -3.4 | -1.9 | 0.7 | 1.6 | -2.8
15KHz multi-tone6 rep16 | -8.9 | -8.6 | -10.2 | -11.3 | -8.2 | 1.3 | 3.1 | -9.4
15KHz multi-tone6 rep64 | -12.6 | -12.8 | -14.3 | -15.2 | -11.7 | 1.4 | 3.5 | -13.3
15KHz multi-tone3 rep2 | -4.9 | -4.9 | -5.6 | -5.8 | -4.8 | 0.5 | 1.0 | -5.2
15KHz multi-tone3 rep16 | -10.7 | -10.7 | -11.3 | -12.6 | -10.3 | 0.9 | 2.3 | -11.1
15KHz multi-tone3 rep64 | -14.6 | -15.0 | -14.5 | -16.5 | -14.2 | 0.9 | 2.3 | -14.9
Ideal Simulation results: the results are aligned well

## Slide 6: NPUSCH format 1:Practical results - 1
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE | Ref. SNR
3.75KHz rep1 | -2.6 | -2.5 | -1.0 | -2.5 |  | 0.8 | 1.6 | -2.1 | -2.1
3.75KHz rep16 | -11.2 | -10.2 | -10.2 | -9.2 |  | 0.8 | 2.0 | -10.2 | -10.2
3.75KHz rep64 | -15.0 | -13.9 | -13.8 | -11.9 |  | 1.3 | 3.1 | -13.6 | -13.6
15KHz single rep1 | -2.6 | -2.1 | -1.1 | -3.1 | -2.1 | 0.7 | 2.0 | -2.2 | -2.2
15KHz single rep16 | -10.1 | -9.5 | -8.6 | -10.0 | -8.4 | 0.8 | 1.7 | -9.3 | -9.3
15KHz single rep64 | -14.5 | -13.1 | -12.5 | -13.7 | -12.0 | 1.0 | 2.5 | -13.2 | -13.2
Practical Simulation results:
Final NPUSCH format 1 single-tone for both 3.75KHz and 15KHz subcarrier spacing performance requirement can be set as per the above averaged practical simulation results. Same as proposal by R4-1609543 from Ericsson.

## Slide 7: NPUSCH format 1: Practical results - 2
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE | Ref.SNR
15KHz multi-tone12 rep2 | 0.6 | 0.3 | 0.4 | -0.8 |  | 0.6 | 1.4 | 0.1 | 0.1
15KHz multi-tone12 rep16 | -6.9 | -6.1 | -7.5 | -8.7 |  | 1.1 | 2.6 | -7.3 | -7.3
15KHz multi-tone12 rep64 | -10.1 | -10.1 | -11.4 | -12.7 |  | 1.3 | 2.6 | -11.1 | -11.1
15KHz multi-tone6 rep2 | -1.0 | -0.6 | -0.5 | -1.9 |  | 0.6 | 1.4 | -1.0 | -1.0
15KHz multi-tone6 rep16 | -7.4 | -6.6 | -7.2 | -9.3 |  | 1.1 | 2.7 | -7.6 | -7.6
15KHz multi-tone6 rep64 | -10.6 | -10.8 | -11.3 | -13.2 |  | 1.2 | 2.6 | -11.5 | -11.5
15KHz multi-tone3 rep2 | -3.4 | -2.9 | -2.6 | -4.3 |  | 0.7 | 1.7 | -3.3 | -3.3
15KHz multi-tone3 rep16 | -9.2 | -8.7 | -8.3 | -10.6 |  | 1.0 | 2.3 | -9.2 | -9.2
15KHz multi-tone3 rep64 | -12.6 | -13.0 | -11.5 | -14.5 |  | 1.2 | 3.0 | -12.9 | -12.9
Practical Simulation results:
Final NPUSCH format 1 multi-tone cases performance requirement can be set as per the above averaged practical simulation results. Same as proposal by R4-1609543 from Ericsson

## Slide 8: NPUSCH format 2:Ideal results
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE
3.75KHz rep1 | 2.2 | 0.5 | 5.3 | 3.9 |  | 2.1 | 4.8 | 3.0
3.75KHz rep16 | -12.2 | -7.7 | -9.0 | -9.0 |  | 1.9 | 4.4 | -9.5
3.75KHz rep64 | -18.6 | -12.8 | -15.0 | -14.3 |  | 2.5 | 5.8 | -15.2
15KHz single rep1 | 2.3 | 2.2 | 5.0 | 3.2 | 3.3 | 1.1 | 2.8 | 3.2
15KHz single rep16 | -10.1 | -6.8 | -6.0 | -7.5 | -9.1 | 1.7 | 4.1 | -7.9
15KHz single rep64 | -17.0 | -11.2 | -12.8 | -14.0 | -14.2 | 2.1 | 5.8 | -13.8
Ideal Simulation results for ACK missed detection probability: large span for each case

## Slide 9: NPUSCH format 2:Practical results
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE
3.75KHz rep1 | 3.7 | 2.5 | 8.3 | 5.4 |  | 2.5 | 5.8 | 5.0
3.75KHz rep16 | -10.2 | -5.7 | -6.0 | -7.0 |  | 2.1 | 4.5 | -7.2
3.75KHz rep64 | -16.6 | -10.8 | -12.0 | -12.3 |  | 2.5 | 5.8 | -12.9
15KHz single rep1 | 3.8 | 4.2 | 8.0 | 4.7 | 5.3 | 1.7 | 4.2 | 5.2
15KHz single rep16 | -8.1 | -4.8 | -3.0 | -5.5 | -6.5 | 1.9 | 5.1 | -5.6
15KHz single rep64 | -15.0 | -9.2 | -9.8 | -12.0 | -11.5 | 2.3 | 5.8 | -11.5
Practical Simulation results for ACK missed detection probability: large span for each case
How to solve the large span from companies, as per RAN4#80bis meeting: additional margin [x dB] may be added into the averaged practical simulation results. See next page

## Slide 10: Extra margin for NPUSCH format 2
Option 1: Add 1 dB to companies’ averaged values with impairments to specify NPUSCH format 2 requirements (R4-1609543 from Ericsson;
Option 2a: Add the STD from ideal results to companies’ averaged values with impairments;
Option 2b: Add the STD from practical results to companies’ averaged values with impairments (R4-1609242 from Nokia);

## Slide 11: NPUSCH format 2:Practical results + margin from Option 1
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE | Ref. SNR
3.75KHz rep1 | 3.7 | 2.5 | 8.3 | 5.4 |  | 2.5 | 5.8 | 5.0 | 6.0
3.75KHz rep16 | -10.2 | -5.7 | -6.0 | -7.0 |  | 2.1 | 4.5 | -7.2 | -6.2
3.75KHz rep64 | -16.6 | -10.8 | -12.0 | -12.3 |  | 2.5 | 5.8 | -12.9 | -11.9
15KHz single rep1 | 3.8 | 4.2 | 8.0 | 4.7 | 5.3 | 1.7 | 4.2 | 5.2 | 6.2
15KHz single rep16 | -8.1 | -4.8 | -3.0 | -5.5 | -6.5 | 1.9 | 5.1 | -5.6 | -4.6
15KHz single rep64 | -15.0 | -9.2 | -9.8 | -12.0 | -11.5 | 2.3 | 5.8 | -11.5 | -10.5

## Slide 12: NPUSCH format 2:Practical results + margin from Option 2a
Case | Huawei | Ericsson | ZTE | Samsung | Nokia | STD | SPAN | AVE | Ref. SNR
3.75KHz rep1 | 3.7 | 2.5 | 8.3 | 5.4 |  | 2.5 | 5.8 | 5.0 | 7.1
3.75KHz rep16 | -10.2 | -5.7 | -6.0 | -7.0 |  | 2.1 | 4.5 | -7.2 | -5.3
3.75KHz rep64 | -16.6 | -10.8 | -12.0 | -12.3 |  | 2.5 | 5.8 | -12.9 | -10.4
15KHz single rep1 | 3.8 | 4.2 | 8.0 | 4.7 | 5.3 | 1.7 | 4.2 | 5.2 | 6.3
15KHz single rep16 | -8.1 | -4.8 | -3.0 | -5.5 | -6.5 | 1.9 | 5.1 | -5.6 | -3.9
15KHz single rep64 | -15.0 | -9.2 | -9.8 | -12.0 | -11.5 | 2.3 | 5.8 | -11.5 | -9.4