## Slide 1: WF on urban macro scenario for coexistence study for WP5D on new radio access technology
Nokia, Alcatel-Lucent Shanghai Bell, Qualcomm, Samsung, CATT, ZTE, NTT DOCOMO, Intel
3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14th - 18th November 2016
Agenda Item: 11.3.1
R4-1610569

## Slide 2: Background
Simulation results from different companies have shown that with the current assumptions and parameters for UMa No. 1 and 5 (aka. 200 MHz B/W, 500 m ISD, 80% indoor user ratio):
  > 5% of the UE have <-10 dB SINR in the UL and DL, and thus have 0 throughput, hence the 5%-tile throughput loss of the system is NA.
  > 80% of the UE need to transmit with maximum power to achieve an UL SINR of 15 dB for meaningful throughput.
On the other hand, simulation results from different companies have shown that with the current assumptions and parameters for UMa UL No. 11 (aka. 20 MHz B/W, 300 m ISD, 20% indoor user ratio):
  < 5% of the UE have <-10 dB SINR in the UL and DL, and thus the 5%-tile throughput loss of the system can continue to be used as coexistence metric.
  But 180 MHz (90%) of the UL B/W is left unused.
Simulation results provided in the following slide show that with 200 MHz B/W, 300 m ISD, 20% indoor user ratio
  > 5% of the UE have <-10 dB SINR in the UL and DL, and thus have 0 throughput, hence the 5%-tile throughput loss of the system is NA.

## Slide 3: UE TX power and UL SINR

## Slide 4: Way forward
Adopt the following assumptions and parameters for Uma DL and UL coexistence simulation in order to achieve a meaningful 5%-tile metric, as well as a higher UL B/W efficiency.
Assumptions and parameters:
  200 MHz B/W
  200 m ISD
  20% indoor user ratio (assuming indoor users are mostly served by small cells at mmWave frequency)
Resultant CDFs of UE TX power, as well as DL and UL SINR are provided in the following slides for information.

## Slide 5: UE TX power

## Slide 6: DL and UL SINR