## Slide 1: Way forward on BS RF requirements for NR
Agenda Item: 11.5.3
Document for: Approval
Source: Nokia
3GPP TSG-RAN WG4 #81 Tdoc R4-1610619
Reno, NV, US, 14th – 18th November 2016

## Slide 2: Background
34 contributions were discussed in agenda item 11.5.3 in the NR session
This contribution summaries the issues and agreed WF for BS RF requirements

## Slide 3: NR BS output power accuracy
BS Output power accuraccy requirement is specified as EIRP
  EIRP is directional and the requirement should be met over a range of directions. Follow eAAS WF (R4-1610800)
For other power issues requirements eAAS WF will be adopted for NR

## Slide 4: BS unwanted emissions
Adopt 1MHz resolution bandwidth for defining the mask
Study further the Pros and Cons for both SEM or UEM principle
Boundary between OOB and spurious domain
  Investigate further the options for defining the limit as
    Single fixed boundary for all bands channel BW
    Multiple fixed boundaries based on frequency range
    Variable boundary based on frequency range and channel BW
    Other possible options
Mask to be aligned with ACLR based on co-existence studies
  The basis for the mask are FCC limits and ACLR can be considered as starting point to define the mask, giving the mask both absolute and relative components
  The emissions in the out-of-band domain should reflect the expected ACLR performance by having a relative component corresponding to the ACLR in two first adjacent channelsThe method to define the E-UTRA mask can be considered for NR as well, i.e. considering the link between SEM and ACLR, especially for the second adjacent channel.
Emission scaling
  For <6GHz OTA consider whetherusing the same methodology as in AAS OTA with some modifications to the definitions should be used, or the emissions should be fixed and not scaled for below 6GHz. For >6GHz, do not apply the AAS emissions scaling methodology

## Slide 5: BS TX spurious emissions
Apply 30 MHz (for above 6 GHz) as the lower frequency limit for the spurious emissions requirements, as recommended in SM.329
  For below 6GHz as a conducted and OTA, lower limit is FFS
Adopt 1MHz resolution bandwidth for defining the mask
For 2nd harmonic as upper limit of frequency range for measurements of OTA spurious emissions for NR bands above 13GHz
  Further studies are needed before concluding on how high in frequency it would be reasonable to test and set the requirements
TRP or EIRP metric is an open issue
  Consider adopting the eAAS approach
Whether TRP or EIRP metric follows eAAS decision

## Slide 6: BS classes
For OTA adopt at least minimum distance as a parameter for describing expected deployments for the BS classes, both for below and above 6GHz. Study further whether more parameters are required
For OTA, set of parameters would be a criteria for definition of BS classes. Possible parameters candidates are minimum distance, pathloss, antenna to antenna distance
For the conducted RF requirements of below 6GHz, the existing 3GPP requirements for LTE and MSR including AAS should be re-used for NR as much as possible. However, how to re-use the existing requirements as much as possible (based on the BS classes defined by the parameters of minimum distance or the others such as MCL ) needs further studies
In order to regulate co-existence in BS classes for heterogeneous networks, (approximated) For Medium range and local area BS classes TRP should be used for the power limit