## Slide 1: WF for UE RF Aspects
Qualcomm, Huawei, Sumitomo, Mediatek, [NTT Docomo, Skyworks]
3GPP TSG-RAN WG4 meeting #81 R4-1610620
Reno, Nevada, US, 14 – 18 November, 2016

## Slide 2: UE reference architecture issues
Background:
  R4-1609590, UE reference architecture for NR, Ericsson, Sony
  R4-1609237, Discussion on UE to UE and in-device co-existence between mmW NR and sub-6GHz NR and LTE, Skyworks Solutions Inc.
The purpose to identify possible reference architectures for mmWave is to evaluate the followings,
  Achievable EIRP, EIS, TRx BW, Modulation, Emission levels, other aspects
  Note: assume feasible components for handheld UE implementation in mmWave in this study
Based on the architectures, study key factors due to mmWave frequencies compared to existing LTE reference architecture:
  Use of Fiiltering in mmWave
  Antenna gain, Beamforming range
  Transmitter noise and Harmonic levels
  LO generation (=Phase noise)
  SNDR
  Isolation (especially b/w sub-6GHz and mmW) for both UE to UE and In-device isolation)
  Power consumption
  Other factors
Identify trade-off between each parameter and the appropriate balances

## Slide 3: EIS EIRP Directional requirements
Background
  R4-1609661, On spatial coverage requirement for mmWave NR UE, Sumitomo Elec. Industries, Ltd
  R4-1609917, Consideration of spatial domain on EIRP, DOCOMO Communications Lab.
  R4-1609722, mmWave UE MOP consideration, Huawei, HiSilicon
  R4-1609942, On UE ACLR metric, Ericsson
  R4-1609649, How to define EIS over different beam angles, Qualcomm Incorporated
  R4-1609723, mmWave UE REFSENS consideration, Huawei, HiSilicon
  R4-1609598 Overview of NR UE Test Proposals in NF and FF, ROHDE & SCHWARZ
Study feasibility of defining EIS and EIRP requirement to guarantee system performance
  CDF in R4-1609649 or other solutions are not excluded
  Antenna array types used in co-existence study can be used as reference
  Study testing time and number of points for EIS and EIRP in order to guarantee the performance with minimum test burden
Study feasibility of defining multiple UE types
  UE types with different spatial coverage, e.g. smartphone, fixed mount device, laptop
  Assume smart phone as the baseline
    Full sphere is FFS. If full sphere cannot be achieved, other solutions to compensate the insufficient EIRP ranges shall be identified.
  How to categorise the UE type is FFS

## Slide 4: EIRP Power classes
Background:
  R4-1609665, On Introducing High EIRP UE for NR, Sumitomo Elec. Industries, Ltd
  R4-1609808, EIS definition for UE in mmWave, NTT DOCOMO INC.
Study how to specify different power classes for EIRP based on evaluations in previous slides.
Develop requirements for one power class as priority

## Slide 5: ACLR
Background:
  R4-1609816, On ACLR with Beamforming, Qualcomm Incorporated
  R4-1610279, On mm wave ACLR for 45GHz and 70GHz, Ericsson France S.A.S
  R4-1609667, The impact of IM3 and input PSD on ACLR, ZTE Corporation
  R4-1609942, On UE ACLR metric,Ericsson
  R4-1609591, On mm-wave UE ACLR for 30, 45 and 70 GHz, Ericsson
ACLR to be defined in TRP
Study feasible ACLR levels for mmWave UE

## Slide 6: SEM
Background:
  R4-1609648, Non-contiguous allocations and MPR with OFDM, Qualcomm Incorporated
  R4-1609868, Metric on UE RF Tx requirements in mmWave, NTT DOCOMO, INC.
  R4-1610166, Simulation of results for NR coexistence study: summary and ACIR proposals, Qualcomm Incorporated
  R4-1609350, Consideration on operating band unwanted emissions, Samsung
  R4-1609418, Further consideration on spectrum emission mask, Huawei, Hisilicon
  R4-1610010 Link budget considerations for radiated modulation quality measurements, ROHDE & SCHWARZ
Study feasibility of FCC emission requirements for defining SEM for mmWave
  Up to 10 % of Channel BW: -5 dBm / MHz
  From 10 % onwards: -13 dBm / MHz
Assume SEM is measured as TRP with fixed BF (i.e., not to integrate the peak of beams)
Assume different numerologies and RB allocations

## Slide 7: Emissions
Background
  R4-1609870, UE to UE coexistence between below 6 GHz and mmWave, NTT DOCOMO, INC.
  R4-1609627, NR unwanted emissions for BS and UE, Ericsson
  R4-1609237, Discussion on UE to UE and in-device co-existence between mmW NR and sub-6GHz NR and LTE, Skyworks Solutions Inc.
UE-to-UE co-existence
  mmWave -> sub-6GHz
    -50dBm/MHz should be guaranteed by TRP.
  Sub 6GHz -> mmWave
    Study if -50dBm/MHz can be satisfied based on legacy devices (e.g. PA, Filter, Switch)
    In parallel actual required level should also be investigated from system point of view.
Study feasibility of general emission requirement of -30 dBm / MHz
  Consider feasibility of post PA filtering
  Study harmonics and other spurious

## Slide 8: NSA device IDC study
  Background contributions
    R4-1609237, Discussion on UE to UE and in-device co-existence between mmW NR and sub-6GHz NR and LTE, Skyworks Solutions Inc.
Study in-device co-existence between sub-6GHz and mmWave
  Required and achievable isolation (including PCB) between them.
  Harmonic levels and noise and LO mixing issue
  IMD generated between sub-6Hz and mmWave TX
  Receiver blocking
  Other expected NSA issues

## Slide 9: Blocking & ACS
Background documents for this topic
  R4-1609756, Out-of-band blockers in the mm-wave spectrum, Qualcomm Incorporated
  R4-1610006, NR blocking requirements for mmWave, Huawei, Hisilicon
Out of band blocking
  Study radio environment at NR mmWave to identify worst case blocking scenarios and required attenuation
  Study feasibility of requirements within following options
    Blocker from UE receive beam peak direction
    Blocker from all directions
    Blocker from one randomly selected direction
In-band blocking
  Study feasible scenarios for in-band blocking assuming
    Co-located NR BS
    Non-colocated NR BS
  Study feasibility of blocker levels for UE
    Assume blocker from outside receiver beam direction
    Assume blocker from UE receive beam peak direction
ACS
  Study feasible ACS levels for mmWave UE
  Study feasilibity and impact ro requirements of defining requirements
    For beam direction
    As TRP, measured over all angles

## Slide 10: Other OTA requirements
Reference
  R4-1609868, Metric on UE RF Tx requirements in mmWave, NTT DOCOMO, INC.
All conventional (conductive) requirements should be specified as OTA requirements in mmWave for NR.
Below requirements in mmWave should be specified in at least for peak beam direction.
  Tx maximum output power (already agreed)
  PCMAX
  Minimum output power
  ON/OFF mask
    Study if BF could impact the result during OFF period
  Power control
  Signal quality (Frequency error, EVM, Carrier leakage, In-band emissions)
  Rx spurious emission
  Maximum input level
    Study how to feed high wanted signal power
Below requirements in mmWave should be specified in at least for TRP with fixed BF
  Occupied BW
  Tx OFF power
    Study if BF could impact the result during OFF period
  Tx Intermodulation