## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei, HiSilicon, Ericsson, Qualcomm, Intel
WF on LAA performance requirements extension
R4-1610639

## Slide 2: Background
During RAN4#80bis meeting, discussion about LAA extension happened.
Extension method:
  Option 1: Extend CCs only in unlicensed band while keeping one CC in licensed band
  Option 2: Extend CCs both in licensed and unlicensed band
DL Burst transmission model
  Need to consider how to define burst transmission model for more than 2 CCs in unlicensed band

## Slide 3: How to handle extension of LAA tests
Extension of LAA performance requirements to multiple LAA SCells will be discussed under TEI14 agenda not Rel-13 LAA WI in the future meeting.

## Slide 4: Rel-13 LAA extension- Performance test
Option 1: Performance requirements are defined for one CC in licensed band and multiple CCs in unlicensed band(s)
  LAA test will focus on verification of performance for detection of LBT burst, AGC, time and frequency tracking, and demodulation on partial sub-frames in both LAA single carrier and aggregation mode
  Performance of aggregated licensed CC can be verified by CA demodulation performance requirements.
    If following Option 2 in page 2, carrier aggregation performance verification on licensed CC will be duplicated
    If the largest aggregated bandwidth is achieved by CA configurations without LAA CC for the UE under test, the maximum receiving capability and performance can be verified by CA tests
    If the largest aggregation bandwidth is achieved by CA configurations with LAA CC for the UE under test, the maximum receiving capability can be verified by SDR tests

## Slide 5: Rel-13 LAA extension- Performance test
Option 2: Performance requirements are defined for multiple CCs in licensed band(s) and multiple CCs in unlicensed band(s).
  Test Applicability rule is defined as:
    For each supported CA capability, if UE passes corresponding CA test with CA configuration that has the largest aggregated licensed CA bandwidth and unlicensed CA bandwidth combination selected from the configurations with largest aggregated unlicensed CA bandwidth combination, the test coverage for the configuration with LAA Scell(s) can be considered fulfilled without executing CA tests for LAA performance requirements.

## Slide 6: Rel-13 LAA extension – SDR tests
Define new SDR tests for LAA
  Test Applicability rule is defined as:
    If the largest aggregated bandwidth is achieved by both CA configuration(s) with or without LAA CC(s), select CA configuration without LAA CC(s) for the test
    If the largest aggregated bandwidth is achieved by CA configuration(s) with LAA CC(s), select CA configuration with LAA CC(s) for the test
  For detailed information, please refer to R4-1610862.

## Slide 7: Rel-13 LAA extension – 10MHz
Only 20MHz LAA performance requirements will be specified, if the CA configurations with LAA CCs support both 10MHz and 20MHz for LAA CCs at the same time.

## Slide 8: DL LBT model for channel access on multiple CCs
Each unlicensed CC independently performs the LBT as defined in B.8 of TS 36.101;
Starting points of LBT burst across LAA CCs will be at the same OFDM symbols.
The burst transmission length:
  Option 1: Each unlicensed CC independently choose its own burst length;
  Option 2: All unlicensed CCs have the same burst length.