## Slide 1: TM9 Test 8.3.1.1 #2 with 4Rx
Intel, [Qualcomm] , [Ericsson] , [Huawei]
3GPP TSG-RAN WG4 Meeting WG4 Meeting #81 Reno, Nevada, USA, 14 - 18 November 2016
R4-1610641

## Slide 2: Background
In RAN4 #81, companies shows different performance observations in 4RX TM9 multi-user test cases. About 3dB difference among 4-RX AP UE performance is found.
2-AP duplicated connection is not proper for IRC-type UE performance evaluation.
 | 2RX AP Performance | 4RX AP Performance
8.3.1.1 (FDD) 70% Throughput |  | 
Intel R4-1609065 | 18.9dB | 13.8dB
QC R4-1609714 | [18.5]dB | [13.7]dB
Huawei R4-1609489 | 16.9dB | 10.7dB
Ericsson R4-1609895 | 17.9dB | 11.2dB
8.3.2.1A (TDD) 70% Throughput |  | 
Intel R4-1609065 | 18.9dB | 13.9dB
QC R4-1609714 | [18.5]dB | [14.2]dB
Huawei R4-1609489 | 17.1dB | 10.7dB
Ericsson R4-1609895 | 17.8dB | 11.1dB

## Slide 3: Way-forward
RAN4 replaces TM9 MU Tests with 4-RX AP UE Tests.
In RAN4#82, interested companies are encouraged to provide 4-RX AP UE performance of tests below
  8.3.1.1 (FDD), 8.3.2.1A(TDD)
  8.3.1.1H (FDD), 8.3.2.1I (TDD)