## Slide 1: WF on link-level simulation assumptions for BS IC
China Telecom, Huawei, ZTE, Nokia
3GPP TSG-RAN WG4 Meeting #81
Reno, Nevada, USA, 14 - 18 November, 2016
R4-1610661

## Slide 2: Background: agreements in RAN4 #80bis
Performance Metric:
  Option 1: compare the target user throughput between advanced receiver and baseline receiver
  Option 2: compare the sum of throughputs of all the intra-cell users between advanced receiver and baseline receiver
  Other option not precluded
Bandwidth: 10MHz
PRB allocation:
  Option 1: full PRB allocation
  Option 2: 6 PRB in the middle of the channel bandwidth.
UE Tx antenna number: 1
BS Rx antenna number:
  Option 1: 2, 4, 8
  Option 2: 2, 4 as baseline, and FFS on 8

## Slide 3: WF (1)
Use fixed reference channels
PRB allocation
  use full PRB allocation
  Note: the PRB allocation is aligned for all the UEs involved in the simulation
Rx antenna number: Cover 2, 4 and 8Rx; Prioritize 2 and 4 Rx
Timing delay and frequency offset
  Option 1: No timing delay and frequency offset for all the intra-cell and inter-cell UEs.
  Option 2: Non-zero timing delay and non-zero frequency offset for the intra-cell UEs, zero timing delay and frequency offset for the inter-cell UEs.
Propagation condition
  As baseline, (EPA5 low, ETU5 low), (EVA70 low, ETU70 low)
  Note: the first element is for intra-cell users and the second element is for inter-cell interferers
DMRS configuration
  Assign the same base sequence and different phase rotations/cyclic shifts for co-scheduled intra-cell UEs, and assign different base sequences for UEs associated with different cells.
  Further discuss the details on base sequence and phase rotation configuration in the next meeting.

## Slide 4
MCS level
  For cases with equal SNR:
    As starting point, use MCS 6, 10, 15 for 2Rx BS, and use MCS 10, 15, 20 for 4/8 Rx BS.
    Note 1: use the same MCS for the multiple co-scheduled UEs
    Note 2: only MCS 10, 15 are used for 2/4/8 Rx BS in the initial simulation (listed in the next page) in order to reduce simulation workload
  For cases with unequal SNR: discuss further in the next meeting
Performance metric & Simulation output
  For cases with equal SNR: Provide throughput v.s. SINR curves for each intra-cell UE for the reference receiver and baseline receiver
    Note 1: Companies to report whether or not the intra-cell inter-user interference is included in the “I” part of SINR in the simulation
    Note 2: the signal power in “S” part is the power of one intra-cell UE
  For cases with unequal SNR: discuss further in the next meeting
WF (2)

## Slide 5: WF (3)
Simulation cases towards the next meeting in Feb 2017
  Simulation cases for 2Rx:
  Simulation cases for 4/8Rx:
Case No. | No. of co-scheduled UEs | Propagation condition | MCS level (intra-cell UEs) | Inter-cell interference scenario
1-1 | 2 UEs with equal SNR | (EPA5 low, ETU5 low) | MCS10 (QPSK 0.61) | High interference level in HetNet: DIP1= -0.43 dB
1-2 |  | (EVA70 low, ETU70 low) | MCS15 (16QAM 0.5) | Low interference level in HomNet: DIP1 = -5.45 dB
Case No. | No. of co-scheduled UEs | Propagation condition | MCS level (intra-cell UEs) | Inter-cell interference scenario
2-1 | 4 UEs with equal SNR | (EPA5 low, ETU5 low) | MCS10 (QPSK 0.61) | High interference level in HetNet: DIP1 = -0.43 dB
 |  |  |  | High interference level in HetNet: (DIP1, DIP2) = (-0.43, -13.78) dB
2-2 |  |  |  | 
2-3 |  | (EVA70 low, ETU70 low) | MCS15 (16QAM 0.5) | Low interference level in HomNet:DIP1 = -5.45 dB
2-4 | 2 UEs with equal SNR | (EPA5 low, ETU5 low) | MCS10 (QPSK 0.61) | High interference level in HetNet: DIP1 = -0.43 dB
 |  |  |  | High interference level in HetNet: (DIP1, DIP2) = (-0.43, -13.78) dB
2-5 |  |  |  | 
2-6 |  | (EVA70 low, ETU70 low) | MCS15 (16QAM 0.5) | Low interference level in HomNet:DIP1 = -5.45 dB
  No timing delay and frequency offset for all the intra-cell and inter-cell UEs are assumed as baseline for the initial simulation submitted for the next meeting.
  Interested companies are invited to provide results for the above cases, and it is FFS whether all the results will be captured in the TR.

## Slide 6: For information: Other simulation assumptions
Parameters | Values
Cyclic prefix | Normal
HARQ RV sequence | 0, 2, 3, 1
Maximal number of HARQ transmissions (including 1st Tx and re-Tx) | 4
Frequency hopping, TTI bundling | Disabled
Modulation of inter-cell interferers | 16QAM