## Slide 1: Way Forward on Determination of PRACH CE Levels
Nokia, Alcatel-Lucent Shanghai Bell, Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14th - 18th November 2016
Agenda Item: 5.5.3
R4-1610694

## Slide 2: Background
Before start transmitting PRACH preamble for initial access to the network, eMTC UEs are required to determines the PRACH enhanced coverage (CE) level based on its RSRP measurements of the downlink reference signals.
Due to RSRP measurement error
  An eMTC UE may mistakenly select a lower CE level and then access the network with the PRACH configuration of the lower CE level.
    Consequence: UE may fail in the first initial access attempt, and then increase its CE level for re-access, resulting larger resource usage and longer initial access delays
  An eMTC UE may also mistakenly select a higher CE level and then access the network with the PRACH configuration of the higher CE level.
    Consequence: UE will use too much extra resource than needed for the initial access attempt, and also result in longer initial access delays.
  The penalty for a wrong selection of the higher CE level is in general much larger than the penalty for a wrong selection of the lower CE level in terms of the PRACH resource waste, since the resource usage for a higher CE level may be multiple times more than a lower CE level.

## Slide 3: Proposed Solution 1
If the PRACH CE level determined with the measured RSRP and configured RSRP thresholds is CE X, allow the UE to select the UE to select CE Y (Y<=X)
  In the following figure, when the measured RSRP=RSRPx, the UE may select {CE2, CE1, CE0}. measured RSRP=RSRPy, the UE may select {CE1, CE0}.
  Note: This option is equivalent to allow the UE to add additional INFINIT positive RSRP measurement offset on the measurement RSRP for PRACH CE level determination.
RSRP
RSRP2
RSRP1
CE0
CE1
CE2
Real RSRP
Measured RSRPx
Measured RSRPy

## Slide 4: Proposed Solution 2
PRACH CE level is determined with the measured RSRP plus the maximum UE measurement error
  In the following figure, the UE should select
    PRACH CE 2, when measured RSRP < RSRP2
    PRACH CE 1, when RSRP2 < measured RSRP < RSRP1
    PRACH CE 0, when measured RSRP1 < RSRP .
RSRP
RSRP2
RSRP1
CE0
CE1
CE2
Measured RSRP +
Real RSRP
Measured RSRP
5dB

## Slide 5: Proposed Solution 3
PRACH CE level is determined with the measured RSRP plus the UE measurement bias , which decreases with the improve of RF conditions
  In the following figure, the UE may select
    PRACH CE 2, when measured RSRP < RSRP2
    PRACH CE 1, when RSRP2 < measured RSRP < RSRP1
    PRACH CE 0, when measured RSRP1 < RSRP
RSRP
RSRP2
RSRP1
CE0
CE1
CE2
max
Measured RSRP +
Real RSRP
Measured RSRP
RSRP(SNR, Es/Iot, RSRQ)

## Slide 6: Way Forward
Rel-13: Use currently specified behavior in the Rel-13 specification
Rel-14: Study this issue further and consider the proposed solutions as a starting point for a potential resolution of the issue. Other potential solutions are not precluded
  A potential option to consider for Solution 3 may be to allow the UE to, but not have to, add a positive bias, up to ΔdB, on the RSRP measurements in the determination of the PRACH CE levels. The Δ decreases with the improve of RF conditions.
Send an LS to RAN1/RAN2 to inform RAN4’s decision
Positive bias Δ (dB) | Ês/Iot (dB)
3 | 
6 | 0>
Positive bias Δ (dB) | Ês/Iot (dB)
3 | 
6 | 
9 | 
9 | 

## Slide 7: Potential Proposed Changes in TS 36.133
6.2.3 Requirements for Cat-M1 UEs
In addition to the requirements defined in 6.2.1 and 6.2.2, a Cat-M1 UE shall also execute the random access procedure defined in clause 5.1 in TS 36.321 [17] using the PRACH configuration contained in PRACH-ConfigSIB in TS 36.331 [2]
Determines the enhanced coverage level based on the RSRP measurement and the configured criterion (RSRP-ThresholdsPrach [2]) as defined in section 5.1.1, TS 36,321 [17]. UE is allowed to add but not have to, add a positive bias, up to dB on the RSRP measurements in the determination of the PRACH CE levels.
Positive bias Δ (dB) | Ês/Iot (dB)
3 | 
6 | 0>
Positive bias Δ (dB) | Ês/Iot (dB)
3 | 
6 | 
9 | 
9 | 
NOTE1: in the above solution, other values of are not precluded
NOTE2: other proposals are not precluded