## Slide 1: WF on Demodulation Performance for enhanced SU-MIMO
3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 - 18 November 2016
Agenda Item: 8.31.3.1
R4-1610700
LG Electronics, Huawei, HiSilicon, Intel, Samsung, Ericsson, Qualcomm

## Slide 2: Background
In RAN4#80BIS, WF on feasibility test for enhanced SU-MIMO was agreed to investigate feasibility and specify requirements for enhanced SU-MIMO receiver with 4 receive antennas UEs.
To Specify final test cases for UE demodulation performance requirements, further investigation with other scenarios are needed.
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #82.
  Based on collecting simulation results in RAN4#82, RAN4 will identify target scenarios for performance requirements definition

## Slide 3: Observations for test feasibility
Feasibility of enhanced SU-MIMO receiver from companies’ results
  R-ML receiver is used
    Green : Feasible for test, Yellow : need more evaluation, Red : Infeasible for test
  Green : R-ML receiver provides testable gain in comparison with MMSE receiver
  Yellow : Performance gain for R-ML receiver depends on channel and antenna configuration
  Red: no gain
 | 16QAM | 64QAM | 256QAM
Rank 2 |  |  | 
Rank 3 |  |  | 
Rank 4 |  |  | 

## Slide 4: Evaluation scenarios
Further evaluation scenarios for test feasibility studies
  MIMO Rank 2 scenario
    TM4/9 2x4 + 16QAM
    TM4/9 2x4 + 64QAM
    TM4/9 4x4 + 256QAM
  MIMO Rank 3 scenarios
    TM3 4x4 + 16QAM
    TM3 4x4 + 64QAM
  MIMO Rank 4 scenarios
    TM4/9 4x4 + 16QAM
    TM3 is FFS
  Other scenarios are not precluded.

## Slide 5: Evaluation scenarios
Antenna configuration
  ULA Low correlation
  ULA Medium correlation (α=0.3, β=0.9)
  ULA Medium A correlation (α=0.3, β=0.3874)
  XPOL Medium A correlation (α=0.3, β=0.6, γ=0.2) for only MIMO rank 3 and 4
PDSCH parameters
  Use follow PMI approach for TM4 and TM9 evaluations
  Use 2 CRS APs for TM9 studies
Interference scenarios
  Scenario #1: Noise-limited scenario (i.e. no inter-cell interference)
  Scenario #2: Interference-limited scenarios (i.e. inter-cell interference)