## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei,[Ericsson],[Qualcomm],[Intel],[Nokia]
Way forward on eLAA demodulation performance
R4-1610706

## Slide 2: Background
As per the agreed WID RP-161832, the eLAA core part is complete and corresponding possible UE and BS demodulation performance requirements need to be defined.

## Slide 3: UE demodulation performance
Option 1: No new UE demodulation performance test needs to be defined;
Option 2: Further discussion of whether and how to verify new UE behavior introduced by eLAA is needed.

## Slide 4: BS demodulation performance requirements

## Slide 5: General
New PUSCH demodulation performance requirements need to defined for eLAA
  In Rel-14, one PCell with 20MHz + one LAA Scell with UL and 20MHz will be defined.
    Considering the WID scope in RP-161832 that at least one of CA_1A-46A, CA_2A-46A, CA_3A-46A, CA_7A-46A, CA_41A-46A, CA_42A-46A and CA_46A-66A will be completed for RF.
  Number of UE to be modeled
    Option 1: Single UE is modeled in all the demodulation test
    Option 2: Model multiple UEs with different timing and frequency offset
  Extension for future possible multiple licensed bands + multiple unlicensed bands combinations that have more than 2UL CCs in Rel-14 is FFS if needed.

## Slide 6: General
Starting PUSCH symbol configuration
  Option 1: ‘01’ (25µs in symbol 0);
  Option 2: define tests with all possible configurations. eNBs are tested for all configurations that it supports
  Other options not precluded.
Ending symbol configuration
  Option 1: Up to OFDM symbol 13
  Option 2: Up to OFDM symbol 12
  Option 3: define tests with 12 symbol and 13 symbol. eNBs are tested for all configurations that it supports
UL grant Scheduling
  Option 1: One stage scheduling
  Option 2: Two stage scheduling
Reference receiver:
  MRC

## Slide 7: General
Resource allocation
  Option 1: Only continuous interlace allocation
  Option 2: Both contiguous and non-contiguous interlace allocation
LAA Sell Carrier Scheduling
  Option 1: Self-carrier scheduling for both UL and DL
  Option 2: Self-scheduling on DL and Cross-carrier scheduling on UL
Antenna configuration
  Option 1: 1 Tx; RX: 2 and 4
  Option 2: 1 Tx; RX: 2, 4 and 8
  Other options not precluded
Channel model
  Option 1: EVA5
  Option 2: EPA5
  Other options not precluded
Modulation
  Companies are encouraged to provide input based on test purposes
Test metric: 70% TP

## Slide 8: UL burst transmission model
Option 1: UL burst transmission model needs to be defined
Option 2: No UL burst transmission model needs to be defined.

## Slide 9: 10MHz BW LAA test
No performance requirements for LAA 10MHz bandwidth to be defined