## Slide 1: WF on Enhanced CRS-IM Performance Requirements
Intel Corporation, LGE, Huawei, HiSilicon, Ericsson
3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 - 18 November 2016
Agenda Item: 8.31
R4-1610716

## Slide 2: Introduction
The following CRS-IM enhancements work objectives are captured in the WID:
  Stage 1: Investigate performance benefits and feasibility of using CRS-IM receivers:
  Stage 2: Specify UE demodulation and CSI reporting performance requirements to verify practical CRS-IM operation for the identified scenarios based on the outcome of Stage 1.
Stage 1 includes the following components:
  Identification of target scenarios
  Identification of reference CRS-IM receiver structure assumptions
  Evaluation of CRS-IM performance
RAN4 #80bis agreements
  R4-168638 Way forward on CRS-IM
  R4-168642 WF on simulation assumptions for CRS-IM
This WF provides further agreements on the target scenarios and reference receivers for the Stage 1 investigations of CRS-IM enhancements
Companies are encouraged to provide further inputs on the scenarios and reference receivers performance/complexity analysis in RAN4 #82
  In RAN4 #82 the simulation results will be collected with the purpose to identify target scenarios for requirements definition and confirm reference receiver feasibility
  In stage 2, test cases will be selected based on evaluation on performance gain, UE implementation complexity and test coverage

## Slide 3: Interference Scenarios
Number of explicitly modelled interference cells
  Baseline: 2
  FFS between 1 and 2 for 4 CRS APs + 4RX scenarios

## Slide 4: CRS-IM for PDSCH (1)
Baseline scenarios for further studies
Companies are also encouraged to bring results and analysis for additional scenarios
Other scenarios are not precluded
Test | TM | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  |  | Serv. cell | Interf. cell
1 | TM4 | Non Colliding | 2 | 4 | 4
2 | TM4 | Non Colliding | 4 | 2 | 2
3 | TM9 | Non Colliding | 4 | 2 | 2
4 | TM4 | Non Colliding | 4 | 4 | 4
Test | TM | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  |  | Serv. cell | Interf. cell
5 | TM4 | Colliding | 2 | 4 | 4
6 | TM4 | Colliding | 2 | 4 | 2
7 | TM4 | Colliding | 2 | 2 | 4

## Slide 5: CRS-IM for PDSCH (2)
Non-colliding CRS Cell ID pattern(S/I1/I2): 0/1/6
Interference profile for PDSCH test cases
  Reuse Rel-13 CRS-IM interference model:
    I1/Noc = 10.45 dB; I2/Noc = 4.6 dB; 20% RU
De-prioritize TM10 CRS-IM enhancements
PDSCH FRC
  Option 1: MIMO Rank 1 + 16QAM 1/2
  Option 2: MIMO Rank 1 + 64QAM 1/2
  Other MCS levels are not precluded and companies to bring inputs on additional scenarios

## Slide 6: Control channel performance
For DL Control Channel tests, investigate whether gain is coming from LMMSE-IRC or from CRS-IM and CRS-IM gains on top of LMMSE-IRC

## Slide 7: CRS-IM for PDCCH/PCFICH (1)
Scenarios
Interference power profile
  Option 1: Reuse Rel-13 CCIM interference power profiles. I1/Noc = 13.91 dB; I2/Noc = 3.34 dB.
  Option 2: Reuse Rel-13 CRS-IM interference power profiles. I1/Noc = 8.36 dB; I2/Noc = 1.66 dB (RU=50%, 50%-tile from 36.863)
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2

## Slide 8: CRS-IM for PDCCH/PCFICH (2)
PDCCH parameters
  CFI
    Test 1: CFI = 2, 3
    Test 2: CFI = 1, 3
  PDCCH AL
    Baseline: AL 2
    Other option is not precluded based on companies’ input

## Slide 9: CRS-IM for PHICH
Scenarios
Interference power profile
  Option 1: Reuse Rel-13 CCIM interference power profiles. I1/Noc = 13.91 dB; I2/Noc = 3.34 dB.
  Option 2: Reuse Rel-13 CRS-IM interference power profiles. I1/Noc = 8.36 dB; I2/Noc = 1.66 dB (RU=50%, 50%-tile from 36.863)
PHICH parameters
  Reuse Rel-13 CCIM PHICH FRC
  PHICH duration:
    Test 1: Extended
    Test 2: Normal
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 2 | 4 | 4
2 | Non Colliding | 4 | 2 | 2

## Slide 10: CRS-IM for EPDCCH
Scenarios
Interference model:
  Option 1: I1/Noc = 13.91 dB; I2/Noc = 3.34 dB, no PDSCH interference
  Option 2: I1/Noc = 10.44 dB; I2/Noc = 4.57 dB, 20% interference loading
  Option 3: I1/Noc = 8.36 dB; I2/Noc = 1.66 dB, 50% interference loading
EPDCCH parameters
  EPDCCH AL = 2
  Localized EPDCCH
Test | CRS pattern | Number of UE RX chains | Number of CRS APs | 
 |  |  | Serv. cell | Interf. cell
1 | Non Colliding | 4 | 2 | 2

## Slide 11: Reference Receivers
Number of cancelled cells for non-colliding CRS-IM
  The PDSCH and DL Control Channels minimum performance requirements are defined under assumption of single dominant interference cell CRS-IM. UEs may be capable for more than 1 cell CRS-IM (up to UE implementation)
CRS-IM receivers for 4 CRS APs ports processing
    Further bring analysis on the performance/complexity for the following non-colliding CRS-IM reference receivers for 4 CRS APs
      Receiver #1: Full complexity four ports CRS-IM processing
      Receiver #2: Reduced complexity CRS-IM processing
CRS-IM assistance information signalling and blind detection
  Companies encouraged to bring inputs on CRS-IM assistance information availability assumptions (e.g. RRC signalling, detection feasibility, etc).

## Slide 12: CRS-IM UE Capabilities
UE capabilities/features framework
  Companies are encouraged to bring inputs on the following questions
    Is new capability needed for R14 CRS-IM?
    Are separate capabilities needed for CRS-IM for data and control channels?
    Are separate capabilities needed for CRS-IM for 2RX and 4RX UEs?
    Are separate capabilities needed for CRS-IM for 2 and 4 CRS APs?