## Slide 1: WF on UE ON/OFF mask for sTTI operation
Ericsson, Huawei
3GPP TSG-RAN WG4 Meeting #81
Reno, USA, 14-18 Nov, 2016
Agenda Item: 10.1.3
Document for: Approval
R4-1610789

## Slide 2: Background
Core requirement related to “Shorten TTI and processing time reduction” WI started in RAN4#81 meeting
Potential impacts on UE ON/OFF mask for sTTI operation is discussed in following contributions:
  R4-1609383: Discussion on UL ON/OFF time mask, Huawei, Hisilicon
  R4-1609501: Discussion on ON/OFF time mask for sTTI, CATT
  R4-1610472: Implication of sTTI operation on UL ON/OFF time mask, Ericsson

## Slide 3: Observation
The UL ON/OFF time mask has some relations to the sTTI performance.
Thus, suitable ON/OFF time mask need to be considered for 2-OS TTI pattern.

## Slide 4: Proposal (1/4)
Define the general ON/OFF time mask for 2-OS TTI as shown below:
The transient period (ramp up or down time ) is [20µs].
The ramp up/down is done outside the TTI duration.

## Slide 5: Proposal (2/4)
When a UE is scheduled across consecutive TTIs, then a single general mask can be used for 2-OS TTI patterns, if there is no power changes between consecutive TTIs
No ramp down/up between consecutive TTIs
The transient period (ramp up or down time ) is [20µs].
The ramp up/down is done outside the TTI duration.
TTI duration
ON level
OFF level
Transient period
TTI duration
Transient period

## Slide 6: Proposal (3/4)
When a UE is scheduled across consecutive TTIs, then following mask can be one of the options for 2-OS TTI patterns, if there is power changes between consecutive TTIs
The middle transient period is [20-40µs].
Companies are requested to study the achieveable transient period in next RAN4 meeting.
TTI duration
ON level
OFF level
Transient period
TTI duration
Transient period
Middle transient period

## Slide 7: Proposal (4/4)
When a UE is scheduled across consecutive TTIs, then another option (wrt to slide 6) of the mask for 2-OS TTI patterns can be as shown below, If there is power changes between consecutive TTIs
The middle transient period is [20µs].
Companies are requested to study the achieveable transient period in next RAN4 meeting.
TTI duration
Transient period
ON level
OFF level
Middle Transient period
Transient period
TTI duration