## Slide 1: Way Forward on EMC requirements for AAS

## Slide 2: From R4-1610446
Proposal 1: Study further whether TX exclusion bands need to be defined to protect the measurement devices. The width of these exclusion bands is FFS.
Proposal 2: Discuss further whether the distance between the EUT and the measurement device for spurious & radiated emissions needs to be increased to mitigate the field strength level to match the existing levels today.
Proposal 3: It needs to be investigated if the BS needs to transmit at full power during all tests or is it sufficient to transmit with a power that generates a field strength level corresponding to the existing EMC requirements for some tests.

## Slide 3: From R4-1610447
Proposal 4: Study further the following possibility:
  Since the RF spurious emissions and EMC radiated spurious emissions can no longer be distinguished, it is proposed to specify a combined spurious emission requirement as a linear sum of RF SE & EMC RE.
  Investiage further the implication of unifying EMC and spurious emissions

## Slide 4: From R4-16010448
Proposal 5:
Study further the following concept for EMC: The level of the interfering signal at the TAB connector should be as defined as TS 37.105 and the interfering signal in the RI test should not be higher than the specified blocking level
Proposal 6:
Study whether mechanisms (such as extending exclusion bands or reducing the RI requirement) need to be defined to ensure that the level of the interfering signal does not increase the existing blocking requirement.