## Slide 1: Way forward on A-MPR simulation assumptions for Band 68
Agenda Item: 8.32.2
Document for: Approval
Source: Airbus DS SLC, Nokia
3GPP TSG-RAN WG4 #81 R4-1610832
Reno, NV, US, 14th – 18th November 2016

## Slide 2: Background
In ECC Decision (16)02, two requirements are defined for LTE signal within 698 – 703MHz frequency range for DTV protection:
  -42dBm/8MHz, for normal environmental conditions
  -30dBm/8Mz, for extreme environmental conditions

## Slide 3: Way Forward
RAN4 to agree on two simulation assumptions sets for the definition of A-MPR requirements (for normal and extreme environmental conditions)
  As proposed in [2] and summarized on the next slide
A-MPR requirements to be defined based on the most stringent simulation assumptions sets
Results based on split-filter approach as discussed in [1] can also be provided.

## Slide 4: Simulation parameters for normal and extreme conditions (from [2])
Tx chain performances |  |  | Worst case relative filter rejection (dB) |  | 
 | Extreme | Normal | Frequency (MHz) | Extreme | Normal
Modulator IQ – image | 28dB | 28dB | 693.5 | 5.7 | 10.9
Modulator carrier leakage | 28dBc | 28dBc | 692.5 | 10.9 | 18.4
Modulator C_IM3 | 60dBc | 60dBc | 691.5 | 18.4 | 26.2
UTRA ACLR 1 | 33dB | 36.5dB | 690.5 | 26.2 | 30.6
 |  |  | 689.5 | 30.6 | 31.7
 |  |  | 688.5 | 31.7 | 32.2
 |  |  | 687.5 | 32.2 | 32.2
 |  |  | 686.5 | 32.2 | 32.2

## Slide 5: References
[1] R4-1609839: Band 68 modifications for PPDR use in Europe, Nokia
[2] R4-1610238: Band 68 compliance with ECC Decision (16)02: Simulation assumptions for normal environmental conditions, Airbus DS SLC