## Slide 1: 3GPP TSG-RAN WG4 Meeting #81 Reno, Nevada, USA, 14 – 18 November 2016
Huawei, HiSilicon, LG Electronics, CATT
Way forward on single-link V2V performance requirements
R4-1610866

## Slide 2: Background
According to the agreements of last meeting, for single-link demodulation tests, PSCCH and PSSCH should defined

## Slide 3: PSSCH demodulation test
Retransmission: 1 time with soft-combining
  Interval between two transmissions: 1ms
Relative timing error (considering Tx and Rx): 24Ts
  FFS whether to take into account V2V signal propagation delay from TX to RX. To be decided in next meeting
Relative frequency error (considering Tx and Rx): 1200Hz
Propagation condition
  Option 1: EVA180, QPSK/16QAM
  Option 2: EVA1500, QPSK
  Option 3: EVA2700, QPSK
  Option 4: EVA1000, QPSK/16QAM
  Other options are not precluded and down selection in next meeting
Bandwidth: 10 MHz and 20 MHz
Consider PSCCH performance when defining PSSCH performance

## Slide 4: PSCCH demodulation test
No retransmission is used
Relative timing error (considering Tx and Rx): 24Ts
Relative frequency error (considering Tx and Rx): 1200Hz
Propagation condition
  Option 1: EVA180
  Option 2: EVA1500
  Option 3: EVA2700
  Option 4: EVA1000
  Other options are not precluded and down selection in next meeting
Bandwidth: 10 MHz

## Slide 5: Test cases handing
CFO and Doppler Shift Estimation Algorithm
  Candidate estimation algorithms
    Method 1: “Single-DMRS” estimation
    Method 2: “Cross-DMRS” estimation
  Performance requirements
    Option 1: V2V minimum demodulation performance requirements are defined based on Method #1
    Option 2: V2V minimum demodulation performance requirements are defined based on Method #2
    Option 3: Different UE capabilities are defined for Methods #1 and #2. Separate V2V minimum demodulation performance requirements are defined for UEs with different capabilities.
Companies are encouraged to provide evaluation results for different options
If results from companies are not aligned, FFS for detailed receiver assumptions

## Slide 6: Simulation assumptions
V2V RX timing window is assumed to be set on CP/2 from the GNSS reference time
Channel estimation interpolation filter in time domain
  Option 1: Linear channel interpolation
  Option 2: Doppler spread conditions adaptive interpolation
  Interested companies are encouraged to provide analyses and other options are not precluded and down select in next meeting