## Slide 1: Way forward on in-band requirements for NR
Agenda Item: 11.5.1
Document for: Approval
Source: Nokia
3GPP TSG-RAN WG4 #81 Tdoc R4-1610921
Reno, NV, US, 14th – 18th November 2016

## Slide 2: Background
10 contributions discussed in agenda item 11.5.1 in NR session
  R4-1609219 Scenarios and assumptions for NR in-band emission, EVM and in-band selectivity requirements with different numerologies, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1609241 Network Assistance in NR waveform selection, AT&T
  R4-1609413 Consideration on In-band emission requirements for mixed numerologies, Huawei, Hisilicon
  R4-1609221 NR UL in-band emissions and EVM requirements at UE TX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1609414 Consideration on In-band selectivity requirements for mixed numerologies, Huawei, Hisilicon
  R4-1609227 NR DL selectivity requirements at UE RX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1609223 NR UL selectivity requirements at BS RX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1609737 Necessity of EVM and in-band emission and its testability for NR BS, NTT DOCOMO, INC.
  R4-1609225 NR DL in-band EVM and emission requirements at BS TX, Nokia, Alcatel-Lucent Shanghai Bell
  R4-1609666 Considerations on EVM requirement in NR, ZTE, ZTE Microelectronics
This contribution summaries the issues and agreed WF for in-band requirements
Scenarios were discussed considering usage of different numerology configurations within a service and with different services

## Slide 3: Scenarios and assumptions
Develop NR DL and UL in-band emission, EVM and in-band selectivity requirements with different numerologies on the same NR Carrier
In first phase define two different numerologies within one NR carrier
  Sub-block 1 with 15kHz SCS
  Sub-block 2 with 60kHz SCS
  Sub-block BWs are FFS and will be investigated in conjunction with other related requirement definitions like EVM and in-band emissions
Develop the in-band requirements for below 6 GHz for different numerologies
Develop the in-band requirements for below 40 GHz for different numerologies

## Slide 4: NR UL in-band emissions and EVM requirements at UE TX
Perform link simulations with two numerologies next to each other in frequency domain to study how stringent UL in-band emission requirements would benefit frequency domain multiplexing of different numerologies within the same spectrum block
Develop first UE Tx in-band emission and EVM requirements for the baseline CP-OFDM baseline waveform assuming suitable spectral confinement methods
If the current LTE based UE Tx in-band emission requirement definition is reused in NR, update the UE Tx in-band emission requirement definition so that both the same and different numerologies are verified as victim and aggressor UEs by checking all the numerologies in the test equipment receiver
  Before agreeing the exact definition of NR UE Tx in-band emission requirement, study if it is feasible to define NR UE Tx in-band emission requirements in a new numerology independent way

## Slide 5: NR DL selectivity requirements at UE RX
Define DL in-band selectivity requirements at UE Rx with different numerologies in adjacent wanted and interfering sub-blocks
Definition in mixed numerology case should follow the same format as uplink, taking the possible power imbalance level between numerologies into consideration
Investigate the necessity of guard band for the targeted modulation

## Slide 6: NR DL EVM and in-band emission requirements at BS TX
EVM is required regardless on single or mixed numerology
  Define two numerology EVM requirements with two sub-blocks with different numerologies
  Further study on the issue that EVMs are unevenly distributed among the allocated resource blocks
  High order modulation up to 256QAM can be studied in the evaluation
Evaluate the feasibility to specify UL based in-band emissions requirement for the BS
In the two numerology case, EVM will be measured for both of the sub-blocks using the numerology used in a given sub-block edge PRBs
  EVM performance of the edge subcarrier shall be covered
Investigate the necessity of guard band for the two numerology EVM requirements
  Evaluate also the feasibility of zero guard band case
  BS scheduler may decide the used guard band
  FFS if granularity is based on PRB or SCS

## Slide 7: NR UL selectivity requirements at BS RX
The uplink in-band selectivity requirement definition in single and mixed numerology case should target for sub-block edge PRB(s)
  Verify the overall performance in addition
Spatial aspects to be considered
RAN4 will use the following assumptions and priorities for developing UL in-band selectivity requirements at BS Rx:
  First requirements using the baseline CP-OFDM signal both for wanted and inferring signals
  Requirements both with the same and different numerologies for wanted and interfering signals
  First requirements using time-aligned wanted and interfering signals. Later requirements for asynchronous cases with non-time-aligned signals
  Investigate suitable guard band between the wanted and interfering signals in case of mixed numerologies and/or non-time aligned signals